## Slide 1: Nuovi rivelatori per nuove diagnostiche in Astronomia X
Marco Feroci
Istituto di Astrofisica e Planetologia Spaziali (IAPS)
Istituto Nazionale di Astrofisica (INAF)
Roma – Tor Vergata

## Slide 2
Science Drivers
Study of matter under extreme conditions of gravity, density and magnetism: simultaneous, high-throughput spectral, timing and polarimetry observations.
Motta et al. 2013
eXTP:
10x the signal to noise

## Slide 3: Outline
Silicon Drift Detectors
  Large-area SDD
  PixDD
Gas Pixel Detectors
Applications to space astronomy
  eXTP (enhanced X-ray Timing and Polarimetry) mission
  IXPE (Imaging X-ray Polarimetry Explorer)

## Slide 4: Enabling Technology: Large-area Silicon Drift Detector e PixDD Diagnostics: High-throughput X-ray spectral-timing (0.5-30 keV)

## Slide 5: The large-area Silicon Drift Detector
SDDs
Heritage of ALICE ITS (LHC) → particle tracking (~1.5 m2 – 300 units, operating since 2008)
R&D INFN, INAF & FBK for X-ray detection
Advantages:
solid state detector
e- drifted and collected by small (~1 mm2) anodes → low capacitance → low series noise
extremely small intrinsic leakage current (< 0.05 nA/anode @ 22° C) → low parallel noise
1D read-out (low power, reduced number of channels)
short drift time (5 µs for 35 mm drift length) → 100% CCE

## Slide 6
SILICON DRIFT DETECTOR
HERITAGE LARGE AREA SDD 25 years of progressive developments
1991
ALICE ITS @ CERN
2002
2007

## Slide 7: The LAD large-area Silicon Drift Detectors
ALICE
2002
ALI2
2010/11
XDXL1
2011/12
XDXL2
2012
ReDSoX
2014/17
Power, Thickness
Low-E QE
Pitch
Size
Low-Ileak

## Slide 8: The LAD large-area Silicon Drift Detectors
ALICE
2002
ALI2
2010/11
XDXL1
2011/12
XDXL2
2012
ReDSoX
2014/17
First full-scale prototypes produced 2014
Cut out from 6” wafer
Geometric area: 120.3 x 72.5 mm2
Sensitive area: 108.5 X 70.0 mm2
Leakage current: <200 pA/cm2 @ Troom
Power, Thickness
Low-E QE
Pitch
Size
Low-Ileak

## Slide 9: Large-area SDD – Performance tests
U19 ASIC Channel | FWHM @ 5.9 keV [eV]
01 | (220.4 ± 2.0)
08 | (234.5 ± 3.0)
17 | (231.0 ± 2.5)
18 | (236.4 ± 2.1)
22 | (237.5 ± 2.2)
26 | (240.5 ± 1.9)
27 | (218.4 ± 2.0)
28 | (218.8 ± 1.9)
VEGA ASIC (Bertuccio et al.)

## Slide 10: Large-area SDD – Radiation tests
NIEL from 11 MeV and 50 MeV protons:
PSI – Zurich
[E. Del Monte et al. 2014, JINST 9]
NIEL from soft protons (800 keV p+):
Tubingen
Variation of the CCE (11 MeV p+)
PSI – Zurich
[Del Monte et al. 2015, JINST 10]
Hypervelocity impacts from debris (0.5-3 mm diameter):
MPIK - Heidelberg
[G. Zampa et al. 2014, JINST 9]

## Slide 11: SDD within Collaboration
Low anode capacitance (few tens of fF)
Low leakage current (tens of pA/cm2)
SDD Quantum Efficiency (QE) > 80%
Notes: Tecnologia SDD principio di funzionamento e caratteristiche e FEE giusta
Descrizione redsox come temi di apllicazione
Dal disegno al prodotto finito

## Slide 12: State of the art SDD for eXTP
Un poco di storia
Familiarizziamo con il principio
ALICE più di 1 m2
raggi X di bassa energia
  Gli sviluppi per Sorgenti di Luce Avanzata
  Gli sviluppi per il passaggio a 6” e la tecnologia LOFT
INFN Trieste
FBK Trento
Elettra Sincrotrone Trieste
INAF IASF INFN Roma 2
INFN INAF Bologna
INFN Pavia
INFN TIFPA Trento
ICTP Mlab Trieste
INFN Firenze Labec
Poli Milano El.&Det.
Since more than 10 years a collaboration of about 40 people is working on general SDD development for various state of the art applications with considerable cross fertilization.
The collaboration is led by INFN-Ts and include: INAF (IAPS-Rm and OAS-Bo), FBK, Politecnico di Milano, Università di Pavia, Elettra Sincrotrone Trieste, Università e INFN di Bologna, ...

## Slide 13
Fondazione Bruno Kessler (FBK)Trentino, Italy

## Slide 14
MNF infrastructure
page
014
  Over 1200 square metres of laboratories:
  2 separated microfabrication cleanrooms (detectors and MEMS)
  1 integration/packaging cleanroom
  1 parametric testing area
  1 materials characterization area

## Slide 15: PixDD - a multi-pixel Silicon Drift Detector

## Slide 16: Enabling Technology: Gas Pixel Detector Diagnostics: X-ray (linear) polarimetry (2-10 keV)

## Slide 17: The Gas Pixel Detector
We developed at this aim a polarization-sensitive instrument capable of imaging, timing and spectroscopy
E. Costa et al. 2001, Bellazzini 2006, Bellazzini 2007
The photoelectric effect
The Gas Pixel Detector

## Slide 18: GPD – Gas Pixel Detector
GEM - Gas Electron Multiplier
Read-out ASIC

## Slide 19: GPD – Gas Pixel Detector

## Slide 20: GPD – Gas Pixel Detector

## Slide 21: GPD – Gas Pixel Detector

## Slide 22: GPD – Gas Pixel Detector

## Slide 23: GPD – Gas Pixel Detector

## Slide 24: GPD – Gas Pixel Detector

## Slide 25: Applications to X-ray astronomy

## Slide 26
The LAD instrument concept
Frame
Collimators
Clamps
SDDs + FEEs
Radiator
542
329
Frame
The Key to LAD:
low weight/power/volume per unit eff. area
unprecedented large effective area
CCD class energy resolution
instrinsic modularity: 40 modules made of 16 SDDs (640 tot.)

## Slide 27: Capillary plate collimators

## Slide 28: Capillary plate collimators
Alternative (proven) technologies:
- Photonis (France)
- Hamamatus (Japan)
Key requirements:
- Lead glass
- Large size: 111 mm x 72 mm monolithic
- 60:1 aspect ratio (83 µm pore, 5 mm thickness)
- High Pb content (>40%)
- Low radioactivity (40K)
- High Open Area Ratio (75%)
- High roughness (>13 nm rms)
- Pore-to-pore alignment (~arcmin)
- Pore-to-surface alignment (~arcmin)
North Night Vision Technology (Nanjing, China)
6.4 keV
17.5 keV
Full-size, 75% OAR

## Slide 29: LAD Module
.....

## Slide 30: LAD Module

## Slide 31: LOFT, eXTP, STROBE-X
LOFT (ESA)
STROBE-X (NASA)
eXTP (CAS)

## Slide 32
eXTP Scientific Payload LAD – Large Area Detector
x4
Total effective area: 3.4 m2 @8 keV
Energy band: 2-30 keV
Energy resolution: <240 eV FWHM @6 keV
Based on the LOFT/LAD design
40 Modules on 2 deployable panels
Collimated, large-area SDD detector. Single photon, <10µs

## Slide 33
eXTP Scientific Payload PFA – Polarimetry Focusing Array
Focal plane imaging polarimeter: 4 optics with 5.25m FL
Imaging, PSF 20 arcsec HPD
Total effective area: 900 cm2 @2 keV (includes QE)
Gas Pixel Detector: single photon, <100µs
Energy band: 2-10 keV
Energy resolution: 20% FWHM @6 keV

## Slide 34: XIPE, IXPE
XIPE (ESA)
IXPE (NASA)

## Slide 35: Payload Components
Deployable Boom with Thermal Sock
(3) MMSS Launch Locks
(3) Detector Units
Detectors Service Unit
Metrology Target
(3) MMSS Bipods
Tip-Tilt-Rotate Mechanism
Metrology Camera
Mirror Module Assembly (3)
MMSS Deck
MMSS Center Tube
Telescopes (3)
X-Ray Shields
Accomplish the science through integrated system of Telescopes and structure alignment components.

## Slide 36: Detector Unit: Grand Summary
INFN
  GPD and associated thermal ctrl
  DAQ and low-voltage boards and associated backplane (through OHB-I)
  Stray-light collimator
IAPS
  Calibration set
  UV filter
OHB-I
  High-voltage board
  Filter and calibration wheel
Stray-light collimator
Filter and Calibration wheel
Housing
GPD
Back-end electronics

## Slide 37: Grazie dell’attenzione
marco.feroci@iaps.inaf.it

## Slide 38: Dense Matter White Paper
Neutron Stars
eXTP
QCD diagram
eXTP
M-R

## Slide 39
Stellar structure equations
EOS
Mass-Radius (M-R)
LOFT must measure both M and R to high precision
(low statistical and systematic errors) for a range of M.
Strong force, equation of state, and mass-radius relation
Notes: How do we translate this into observables?
Animate (1): Fortunately the stellar structure equations (hydrostatic equilibrium) means that there is a direct, and unique relation between the EOS and the mass-radius relation of NS. Each line in left panel corresponds to a line in the right hand panel.
Thus by measuring MR we uniquely determine the EOS.
What do we need to do this? 1. We need both M and R simultaneously. 2. We need multiple measurements, over a range of M. 3. We need small error bars – for any method or source type we need to think about both statistical errors (e.g. do we have enough photons) and systematic errors (in which I include standard systematics, and model dependencies). For the latter, where they exist, aim to mitigate by independent and cross checks.
MR (Mass-Radius)

## Slide 40: Spectral-Timing for strong field gravity
Motta et al. 2013
Strong gravity dynamical frequencies just detected in current (RXTE) data
eXTP diagnoses strong field gravity very precisely by:
  timing of the flux variations
  time resolved spectroscopy
  at very high signal to noise
Uses known phenomena
General Relativity predicts precise
orbital and epicyclic frequencies
at each radius
Orbiting inhomogeneities make frequencies observable
eXTP:
10x the signal to noise
Wellons et al. 2013
SFA  1 keV
Notes: Time series different at different energies
Fourier analysis
15 times the s/n mean 1 sigma effect becomes 15 sigma!
you measure it in 1/225 of the time

## Slide 41: Flux Energy Frame dragging in BHB
Tell-tale sign of precession: a rocking iron line
Ingram & Done (2012)
https://www.youtube.com/watch?v=e1QmLg5mGbU

## Slide 42: Fe-line Tomography with eXTP
30 ks LAD simulation
GX 339-4
130 ks XMM + 70 ks NuSTAR
H 1743-322
Courtesy: Adam Ingram
QPO phase-selected spectroscopy (here 2 phases shown)

## Slide 43: Simultaneous polarization variability in LFQPOs
www.youtube.com/watch?v=ieZYYfCapJg&feature=youtu.be
Ingram et al (2015)
ψ (degrees)
Newtonian
GR
Notes: This is the result of one our our calculations. On the left, we see flux and polarization (position=angle, size=degree). All GR effects are included, and a=0.998 id assumed to wash out variability as much as possible to get a conservative estimate.

## Slide 44: QPO Phase folding: LAD+SFA+PFA

## Slide 45
The LAD instrument concept
Peak effective area: 3.4 m2 @8 keV
Energy resolution: <240 eV FWHM @6 keV
40 Modules on 2 deployable panels
200 eV

## Slide 46: Benefit of an equatorial orbit

## Slide 47: Optical-thermal filters
Key requirements:
- Guarantee the light tightness of the SDD (10-6 attenuation in visible light), while guaranteeing >90% transparency at 2 keV
- Large size (112 mm x 73 mm), monolithic
- Participate in the thermal balance of the LAD Module
Technology at IHEP/CAS (Beijing, China)
Implementation:
- 1 µm thick Polymide
- 120 nm one-sided Al coating
Heritage: HXMT filter (1 year in orbit)
Development: full-size prototype already produced. Tests ongoing.

## Slide 48: GPD – Gas Pixel Detector

## Slide 49: GPD – Gas Pixel Detector

## Slide 50: eXTP concept
Payload concept
  Short focal-length for multiple modules
  Deployable panel for collimated modules
  Polarimeter with imaging capability
  Wide field monitor
x9
x4

## Slide 51
Five white papers for eXTP science case:
Dense Matter 😀 accepted
Strong Field Gravity 😊 under revision
Strong Magnetism 😀 accepted
Obs. Science Paper 😀 accepted
Instrument and mission 😒 to be submitted soon
eXTP Science Drivers
Study of matter under extreme conditions of gravity, density and magnetism: simultaneous, high-throughput spectral, timing and polarimetry observations.
Wide-field monitoring for transients (and e.m. counterparts of GWs) and rapid follow-up.
Large Science Working Groups.