## Slide 1: Serial port Com with Python
Amongst the many possibilities of Python, communication with the Serial (COM) port of the computer where it is running ranks very high.
The key library is pySerial, see for details:
  https://pyserial.readthedocs.org/en/latest/index.html
An important introductory example is to detect the available serial ports, on Python prompt enter: (pySerial needs to be installed)
  >> from serial.tools import list_ports
  >> list_ports.comports()
  Python OUT >>
[['/dev/cu.Nokia206-COM1', 'n/a', 'n/a'],
['/dev/cu.Bluetooth-Modem', 'n/a', 'n/a'],
['/dev/cu.usbmodem411', 'Arduino Due Prog. Port', 'USB VID:PID=2341:3d SNR=95238343334351C02112']]
In the example an Arduino DUE is connected to port 411. The example is described in:
http://stackoverflow.com/questions/12254378/how-to-find-the-serial-port-number-on-mac-os-xhttp://stackoverflow.com/questions/12254378/how-to-find-the-serial-port-number-on-mac-os-x

## Slide 2: Python Serial communication, cont.
Next step is to use Python to control a device, see: www.akeric.com/blog/?p=1140
Create and upload the Arduino Module SerialPythonRX, as in the webpage.
Connect Arduino ™ to the computer via USB and Detect the name of serial port
Open a Python session and enter:
  >> import serial
  >> ser = serial.Serial('/dev/tty.usbmodem411', 9600)
  >> ser.write('5’)
the LED connected to pin 13 will blink 5 times. Make sure to use correct Serial port name.
Arduino is a programmable prototyping board based on a ATMega processor, connected via USB to the control computer.