## Slide 1
Risultati della fase 1 di Multipinch
Franco Alladio
WiP – 14 Luglio 2014

## Slide 2
PROTO-SPHERA
A spherical tokamak where the metal centerpost is replaced by a plasma centerpost:
will the plasma centerpost be able to produce and drive the plasma ring?
Anode and Cathode needed for setting up the configuration

## Slide 3
Anode
Cathode
Directly heated W-Mo cathode, hollow gas puffed W-Cu anode
cathodes very similar to
‘ice-age’ Ural spirals!
Ural spirals
OOPartifacts
150 ky old?
W & Mo

## Slide 4
First load assembly tests central plasma column
“Multipinch”, no compression PF coils, no torus
only shaping PF coils, pinch current < 10 kA
Annular hollow anode
Annular heated cathode
6 Cathode modules with rotating AC heating field

## Slide 5
PROTO-SPHERA Part 1b: annular cathode, annular anode
PROTO-SPHERA Part 1a: annular cathode, cylindrical anode
Phase 1 Simple cylindrical element as anode: aim of first experiment was plasma breakdown*
*risk of annular anode is plasma arc anchoring

## Slide 6
Present status of hardware
3 Power supplies: Cathode AC 6-phased heaters, PF Coils & Pinch  Load assembly
Cathode heating
power supply
Pinch & PF coils
currents power supplies

## Slide 7
Breakdown July 3 2014, anode at 170 V (half of 350 V max of power supply)
then plasma sustained by 65-75 V
but… true breakdown
lost at the third shot!
Cathode heated > 50 cycles:
no problems whatsoever

## Slide 8
Parasitic current path near inner vessel
evidence from light emission & magnetic measurements

## Slide 9
Evidence of parasitic current paths
from sparks near vessel
and light and near vessel

## Slide 10
Proposed cure for parasitic current path:
build & install immediately PROTO-SPHERA
divertor supports, machine ready to host them
Vacuum vessel will become thrice-partitioned
Inox
divertor supports

## Slide 11
Move from cylindrical to annular anode at the same time

## Slide 12
Crab Nebula
Hopf foliations
(4D sphere projected in 3D)
Smoke rings, air bubble rings, plasma rings: a jet drives them all