## Slide 1: Long-pulse operation of the PFRC-2 device
S.A. Cohen, B. Berlinger, C. Brunkhorst, M.E. Edwards, P. Jandovitz, J. Matteucci, C.E. Myers, and C. Swanson
Princeton Plasma Physics Laboratory, Princeton University, Princeton, NJ
PFRC-2 device at PPPL
p
Hi-T Superconducting FCs
rs to 7 cm
Te to 400 eV
td to 250 ms

## Slide 2
Take-away points
Research aimed at small (1-10 MW), clean, fusion reactors
for niche applications.
Flux conservation is critically important.
Wall (PMI) interactions should be minimized.
Separatrix should be well away from wall.
Fueling techniques critically important.
Stable discharge durations (250 ms) exceed 105 tAlfven.
Rotating interchange modes stabilized by gas puffing.

## Slide 3: Outline
Long pulse: to 250 ms
Superconducting flux conservers (Hi-T SC FCs)
RMFo heating of the PFRC-2
Gas puffing: refueling
The PFRC-2
An FRC embedded in an axisymmetric tandem mirror
Hi-T SC FCs
Bz
Gas puff
m-wave
Ha
X ray
X ray
RMF

## Slide 4
Why long pulse – what is long pulse?
RF times scales
Instability time scales
CD/Inductive time scales
Energy time scales
Ash exhaust/reactor time scales
LHD
Tilt
Interchange
PMI
PFRC-2

## Slide 5
1988 ANS (J. Plasma Phys. 40, 127) t = 15 ms
1989 Flinders (Pl. Phys. Cont. Fus. 32, 575) t = 50 ms
1991 Flinders (Rev. Sci. Instr. 62, 1787) t = 40 ms
1995 Flinders (Pl. Phys. Cont. Fus. 37, 209) t = 50 ms
2009 Prairie View (PRL 102, 255004) t = 40 ms
Other long-pulse FRCs
2015 TriAlpha (Nature 6, 6897) t = 7-15 ms
No flux conservers

## Slide 6
High-Temperature Superconductor FCs

## Slide 7
Characteristics
  Frequency = 8.025 MHz
  Odd parity
  Pforward to 25 kW (200 kW); Preflected ~ ¼%
  Pabsorbed ~ 35-75% Pf
  Duty factor 1%
Predicted benefits
  Closed field lines
    Matteucci poster
  Electron heating
    Jandovitz poster
  Ion heating (wRMF~wci)
  Plasma stabilization
    Swanson poster
RMFo heating of the PFRC-2

## Slide 8
Density stays ~constant throughout pulse.
Gas puff only increases ne briefly.
Temporary reduction in ne fluctuations.
Midplane Ha rises, stays high long after gas puff.
  Recycling off room temperature FCs (tFC~ 3 ms @ 70F)
ne behavior with room-temperature FCs
Pf ~ 10 kW, IH = 100 A
Gas puff
2e12/cc
Prefill H2
~ 2e13/cc

## Slide 9
  Behavior with SC FCs at LN2 temperature: (tFC ~ 1 s)
Pulse length scan
Density rapidly decays
Gas puff!
Fluctuations suppressed longer
Absorbed RMF power
Density flattop from 2 ms gas puff persists for 10s to 100s ms
Ha
0 10 20 30 40 50
Time ( ms)

## Slide 10
10 kHz/div, po = 0.66 mT, Pf =8 kW
Behavior ne fluctuations with SC FCs (LN2)

## Slide 11
Effect of gas-puff-time on ne with SC FCs (LN2)
t0 = 0.1 ms
2 ms
7 ms
20 ms
40 ms
Line –average density
Absorbed RMF power
Injecting too early decreases density plateau duration

## Slide 12
Effects of gas puffs in end cell
ne
Ha
-Pend cell
Paddle current
Pa
Biased Paddle
0 20 40 60 ms
3e17 H+/s
For this case Ha increases.
Gas puff stifles ion flow to paddle.
Initial pump out of end cell.
Gas puff raises pressure in end cell
3e-5T
Pf = 10 kW; IH = 130 A
200kHz/div
5MHz/div

## Slide 13
RMF efficiently ionizes central cell gas in < 0.2 ms.
With Hi-T SC FCs, plasma flows into end cells until density in central cell falls, increasing RMF penetration ~ T5/4/n1/2.
Good heating occurs, promoting full RMF penetration.
Current drive & re-distribution: FRC forms
L/R|cl~ 2 ms while L/R|anom~ 20 ms
Confinement improved because FRC formed.
Subsequent gas puff penetrates low-density FRC plasma, is ionized throughout, and decorates the already established FRC field pattern.
Long pulses, via SC FCs, were necessary to see this wall-influenced behavior.
Working model of density behavior

## Slide 14
Profile effects
  Is density increase due to axial contraction or improved confinement?
  Full ne, Te, Ti profiles
  Separatrix
  SOL parameters, including flows
The role of hydrogen implantation in the walls
Ion-electron drag
CD efficiency
Higher field, higher power: ion heating
Open questions (immediate)

## Slide 15: Summary: Long-pulse RC discharges
Flux conservation is critically important.
Wall (PMI) interactions should be minimized.
Separatrix should be well away from wall.
Gas fueling technique has been essential.
Stable discharge durations exceed 105 tAlfven.
Rotating interchange modes stabilized by gas puffing.
A posteriori, surprising long-pulse behavior justifies our decision to built Hi-T SC FCs.
Niche applications
  Spacecraft propulsion (planetary defense, exploration)
  Forward deployment
  Distributed power grid

## Slide 16: Additional slides

## Slide 17: What is odd parity? Symmetry under mirror reflection
Odd
Even

## Slide 18: Closed vs open field lines
Even parity Odd parity
Open field lines are ones that intersect a material object or leave the device.
Better confinement

## Slide 19
Closed field lines work – higher Te

## Slide 20: 1. RMFo electron heating- Lsp (PIC) code
Roach and Cohen (2007)
PFRC Data showing 150-eV electron temperature
LSP simulation between 120 and 150 eV Maxwellian, but with broader energy tail
Fully self consistent, fully electromagnetic
Welch and Cohen (2010)

## Slide 21
Cohen and Glasser (PRL 2000)
Ion heating ( = R/ci)
Threshold
Saturation
Heating to temperatures relevant for aneutronic fuels
0.1 < |R/ci| < 2
BR/Ba < 0.01
Gradient in heating efficiency may allow tuning for isotopes
BR = 128 G
Cohen, Landsman, Glasser (PoP 2007)
Predicted ion heating: r = 10 cm, k = 5, Be = 20 kG

## Slide 22
Milroy
Evidence for closed field lines
Even parity
Odd parity
250 ms long pulse
Separatrix
Fluctuation spectrum
measured by probe
1st Goal: to close field lines, form a separatrix and improve confinement
t ~ 105 tA

## Slide 23
FRC options: The size-field plane
FRCs
Choices
Fuel
Beta
Configuration
Heating method
Nature
E
Size
Stability
Fusion power
Compressed
Helion
ITER
Instability problems