## Slide 1: Modifications to Ideal Stability by Kinetic Effects for Disruption Avoidance
J.W. Berkery, S.A. Sabbagh, and Y.S. Park
Columbia University
R.E. Bell, S.P. Gerhardt, B.P. LeBlanc, and J.E. Menard
Princeton Plasma Physics Laboratory
18th International Spherical Torus Workshop
Princeton, New Jersey
November 3-6, 2015

## Slide 2: Abstract
Marginal stability points of global modes during high beta operation in NSTX can be found by computing kinetic modifications to ideal magnetohydrodynamic limits on stability. Calculations with the DCON code for nearly five thousand experimental equilibria show that the no-wall beta limit decreased with increasing aspect ratio and increasing broadness of the pressure profile, which has implications for NSTX-U. Kinetic modification to ideal limits calculations for several discharges as computed using the MISK code predict a transition from damping of the mode to growth as the time approaches the experimental time of marginal stability to the resistive wall mode. The main stabilization mechanism is through rotational resonances with the ion precession drift motion of thermal particles in the plasma, though energetic particles also contribute to stability. To determine RWM marginal stability for use in disruption avoidance, ideal stability limits need to be modified by kinetic effects in order to reproduce experimental marginal stability points. Guided by the full calculations, reduced stability models are investigated to inform automated disruption characterization and prediction analyses presently being developed using NSTX data for application to NSTX-U.

## Slide 3: Near 100% disruption avoidance is an urgent need for ITER; NSTX-U is planning a disruption avoidance system
The new “grand challenge” in tokamak stability research
  Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption rate: < 1 - 2% (energy load, halo current); << 1% (runaways)
  Disruption prediction, avoidance, and mitigation (PAM) is multi-faceted, best addressed by focused, national effort (multiple devices/institutions)
Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI
Plasma Operations
Avoidance Actuators
q, vf, p control
3D fields: EF, vf control
n=1-3 feedback
Mitigation
Early shutdown
Massive Gas Injection
Control Algorithms: Steer
Towards Stable Operation
Locked Mode, NTM avoidance,
RWM, dynamic EF, state-space
control (plasma response)
Disruption Warning
System
Predictors (Measurements)
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), vf(r),…..)
Plasma response (RFA, …)

## Slide 4: RWM dispersion relation evaluated with ideal and kinetic components allows for passive stabilization of the RWM
Resistive Wall Mode (RWM) fluid dispersion relation:
τw-1 is slow enough for active stabilization (feedback)
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
However, experiments operate above the no-wall limit without active control!
Passive stabilization
  Collisional dissipation
  Rotational stabilization
    Models with scalar “critical rotation” for stability could not explain experiments
[S. Sabbagh et al., Nucl. Fusion 50, 025020 (2010)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink Mode
Resistive Wall Mode
~τw-1

Ideal Stability
Kinetic Effects

## Slide 5: NSTX steadily progressed above the no-wall limit, adding improved active control, understanding of passive stability
li
[S. Sabbagh et al., Phys. Plasmas 9, 2085 (2002)]
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
Pressure peaking factor
[S. Sabbagh et al., Nucl. Fusion 44, 560 (2004)]
Active control
  Dual sensor (Bp + Br) proportional gain
  State space control with model of conducting structures and plasma mode
Passive stability
  Kinetic effects in the RWM dispersion relation
  Stabilizing rotational resonances between particles and mode
[S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)]
active control
passive

## Slide 6: New, expansive DCON calculations confirm previous assessment of the NSTX ideal n=1 no-wall limit
Above the no-wall limit
  DCON runs with consistent settings: Ψhigh < 0.992, dmlim = 1.10 (truncates at q = X.1)
  4784 equilibria from 349 discharges from 2010, all in the flat-top, all with βN/li > 2.5
Below the no-wall limit
DCON assessment of the NSTX no-wall limit (as of 2013)
βN/li ≈ 6.7
βN ≈ 4.3
βN/li ≈ 6.7
βN ≈ 4.3
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]

## Slide 7: The ideal no-wall limit is estimated through dependence on internal inductance, pressure peaking, aspect ratio
DCON
βN = 6.7li
βN = 1.9111(p0/<p>)
βN = 14(A-1-0.4)
Composite estimate
Example: NSTX discharge 138556
ideal n = 1 no-wall limit
kinetically stabilized
operational boundary
kinetically stabilized
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]

## Slide 8: No-wall limit dependencies on internal inductance, pressure peaking, and aspect ratio have implications for NSTX-U
New neutral beams:
Broader current and pressure profiles
New center stack:
Larger aspect ratio
Both new capabilities mean NSTX-U no-wall beta limit should be lower than NSTX
BUT ideal stability is, of course, not the full picture! Kinetic effects must be included…
(NSTX-U: ~2x higher BT, Ip, PNBI and ~5x pulse length vs. NSTX)
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]

## Slide 9: NSTX reaches high βN, low li range of next-step STs and the highest βN/li is not the least stable
NSTX can reach high β, low li range where next-step STs aim to operate
  High βN for fusion performance, high non-inductive fraction for continuous operation
    High bootstrap current fraction -> Broad current profile -> Low li = <Bp2>/<Bp>ψ2
  Unfavorable for ideal stability since low li reduces the ideal n = 1 no-wall beta limit
The highest βN/li is not the least stable in NSTX
  In the overall database of NSTX disruptions, disruptivity deceases as βN/li increases
  Passive stability of the resistive wall mode (RWM) must be explained
[S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)]
[S. Gerhardt et al., Nucl. Fusion 53, 043020 (2013)]
0
li
0.0
0.2
0.4
0.6
bN
li
bN/li
13
12
11
14
8
6
4
2
0
bN
8
6
4
0.0
0.2
0.6
0.8
0.8
bN/li
13
12
11
14
10
10
0.4
Unstable RWM
Stable/Controlled RWM
βN/li = 6.7 : computed
NSTX n = 1 no-wall limit
2
Disruptivity
[J. Berkery et al., Phys. Plasmas 21, 056112 (2014)]

## Slide 10: Kinetic effects arise from the perturbed pressure, are calculated in MISK from the perturbed distribution function
Force balance:
leads to an energy balance:
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved in MISK by using from the drift kinetic equation for
Precession Drift
~ Plasma Rotation
Collisionality

## Slide 11: MISK calculations are grounded in validation against unstable experimental plasmas
MISK calculations (at tMISK) include kinetic effects, have been tested against many marginally stable NSTX experimental cases
NSTX
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]

## Slide 12: MISK calculations generally reproduce the approach towards marginal stability seen in experiments
In each case, the calculations trend towards instability (γτw = 0) as the time approaches the time of experimental RWM instability growth
  Twelve equilibria from discharges with no RWM show no trend and are more stable in the calculations
Thermal particles
with energetic particles
unstable
stable
unstable
stable
NSTX
NSTX
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]

## Slide 13: NSTX-U has new capabilities that impact stability or can be utilized for disruption avoidance
New neutral beams:
- Higher power
- Broader current and pressure profiles
New center stack:
- Higher current, field yields lower collisionality
- Test physics at larger aspect ratio
[S.P. Gerhardt et al., Nucl. Fusion 52, 083020 (2012)]
NSTX-U state-space wf controller w/NTV as actuator
NTV torque density (N/m2)
Plasma rotation (rad/s)
Radial coordinate
NTV
region
0
2
4
6
104
desired wf
t1
t2
t3
[S.A. Sabbagh et al., IAEA FEC paper EX/1-4 (2014)]

## Slide 14: Real-time MHD spectroscopy, active control, or kinetic physics can be used for disruption avoidance in NSTX-U
safe
too high
too low
Ip (MA)
MHD Spectroscopy
  Use real-time MHD spectroscopy while varying ωφ and βN to predict disruptions
  Disadvantage: plasma stability can change when kinetic profiles change, but MHD spectroscopy is limited in frequency
Kinetic Physics
  Need real-time control of plasma rotation to stay in favorable kinetic stability range
  Evaluate simple physics criteria for global mode marginal stability in real-time (<ωE> on resonance)
Active Control
  Combined Br + Bp feedback reduces n = 1 field amplitude, improves stability
  RWM state space controller sustains low li, high βN plasma

## Slide 15: Reduced RWM kinetic stability model for disruption prediction
Resonant Field
Amplification (~1/δWK)
Precession
Bounce
Simple expression for δWK = F(ωφ) will approximate these curves, with simple expressions for precession and bounce frequencies… and with collisionality included
ωφ/ωφexp
NSTX 121083
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
Bounce/transit resonance stabilization
Plasma evolution
Marginal stability
νeff/νexp (marginal stability)
γτw contours vs. ν and ωφ
instability
(experiment)
ωφ/ωφexp (marginal stability)
MISK code
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
Rotation, collisionality dependencies not so easily separable, but simplified, analytical models for these
have been proposed as well.
[J.W. Berkery et al., Phys. Plasmas 18, 072501 (2011)], [Y.Q. Liu et al., Phys. Plasmas 16, 056113 (2009)]
[J. Berkery et al., Phys. Plasmas 21, 056112 (2014)]
[J. Berkery et al., Phys. Plasmas 17, 082504 (2010)]

## Slide 16: Disruption event chain characterization capability started for NSTX-U
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
    Example: RWM marginal stability from kinetic model
    Attack events at several places
    Give priority to early events
  Provide cues to avoidance system to break the chain
  Provide cue to mitigation system if avoidance deemed untenable
t
Disruption Event Characterization And Forecasting (DECAF) code written to address the first step – initial test runs started using NSTX data
[DOE report on Transient events (2015 - in final preparation)]

## Slide 17: Significant physics research is needed to predict opportunities for avoidance in disruption event chain
Examples of gaps in physics understanding
  Prediction of stability in low rotation plasmas
  Accurate non-ideal MHD stability maps
  Physical understanding of how mode locking produces disruption
  More comprehensive, validated physical understanding of role of rotation and profile in MHD stability
trigger
possible (but not required) non-linear global mode initiation by bursting MHD event
n > 0 MHD mode
computed linear kinetic MHD instability limit surpassed, leading to exponential mode growth, or saturated rotating mode slows plasma rotation
excessive δB/B or lock
if n > 0 mode grows, plasma disruption occurs at excessive mode amplitude
if rotating mode locks, will grow to excessive amplitude
global mode may trigger an NTM, spawns an NTM disruption event chain
Example: A typical global MHD mode disruption event chain

## Slide 18: Disruption Event Characterization And Forecasting (DECAF) code is structured to ease parallel development
Physical event modules separated
  Present grouping follows work of deVries – BUT, is easily appended or altered
Warning algorithm
  Present approach follows work of Gerhardt, et al. – BUT is easily appended or altered
General idea:
  Build from successful foundations – BUT keep approach flexible
Main data structure
Code control workbooks
Density Limits
Confinement
Technical issues
Tokamak dynamics
Power/current handling
Mode stability
Physical event modules
Output processing
Kinetic RWM analysis will be used in DECAF as a reduced stability model

## Slide 19
JET disruption event characterization provides framework to follow for understanding / quantifying DPAM progress
[P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018]
P. de Vries disruption event chain analysis for JET performed by hand – need to automate
JET disruption event chains
Related disruption event statistics

## Slide 20
DECAF code yielding initial results: disruption event chains, with quantitative warnings
PRP warnings
PRP
VDE
SCL
IPR
Detected at: 0.420s
0.440s
0.475s
0.485s
NSTX
142270
Disruption
10 physical events are presently defined in code with quantitative warning points
  Easily expandable, portable to other tokamaks
This example: Pressure peaking (PRP) disruption event chain identified by code
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 20 ms after last PRP warning
  (SCL) Shape control warning issued
  (IPR) Plasma current request not met
Kinetic RWM stability model will be implemented in (RWM) event
Event chain

## Slide 21
Sensor/predictor (CY available) | Control/Actuator (CY available)
Low frequency MHD (n=1,2,3): 2003 | Physics model-based RWM state-space control (2010)
Low frequency MHD spectroscopy (open loop: 2005) | Dual-component RWM sensor control (closed loop: 2008)
r/t RWM state-space controller observer (2010) | NTV rotation control (open loop: 2003) (+NBI closed loop ~ 2017)
Real-time rotation measurement (2015) | Safety factor control (closed loop ~ 2016-17)
Kinetic RWM stabilization real-time model (2016-17) | Control of βN (closed loop: 2007)
MHD spectroscopy (r/t) (in NSTX-U 5 Year Plan) | Upgraded 3D coils (NCC) (in NSTX-U 5 Year Plan)
Research in today’s presentation is part of NSTX-U’s evolving capabilities for disruption prediction/avoidance

## Slide 22: Reduction of plasma disruptivity in NSTX-U will require implementing global stability models
Ideal stability is necessary, but not sufficient to explain stability
  Detailed DCON calculations confirm that previous calculations of the no-wall limit for NSTX were relatively accurate
Stabilizing kinetic resonances between plasma rotation and particle motions explain RWM stability
  Addition of kinetic effects yields agreement with marginal point in NSTX
  A real-time estimate of ExB frequency can determine if the plasma rotation is unfavorable and rotation control will return the plasma to a stable state
Disruption Event Characterization And Forecasting (DECAF) code written to identify disruption event chains
  Disruption categories and their sequential connections analogous to those used on JET are adopted, with warning algorithm for NSTX-U
  Reduced marginal stability models from kinetic RWM theory will be implemented in this framework

## Slide 23: Sign up for Electronic Copy of Presentation
Please Include Name and Email Address
Or pick up a reprint…

## Slide 24
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
New center column doubles toroidal magnetic field, plasma current
  Access conditions closer to FNSF
  Pulse lengths increase from 1 to 5 seconds
Second neutral beam injection system
  Doubles heating power, increases flexibility available for experiments
  More tangential injection improves current drive, especially at small plasma current
Increased flexibility in divertor configuration
The National Spherical Torus Experiment Upgrade (NSTX-U) at the Princeton Plasma Physics Lab

## Slide 25: Disruption Prediction is a Multi-disciplined Task
Theoretical investigation
  Understanding of underlying physics of triggers and events required to create and extrapolate prediction algorithms to unexplored frontiers of next-step tokamak operation
Tokamak experiments
  Validate theory and determine reproducibility of the events
Modeling at several levels (e.g. quasi-empirical, linear, non-linear)
  Connect theory and experiment – the basic component of creating prediction algorithms; from r/t modeling coupled to sensors, etc. - to full non-linear MHD
Diagnostics
  Develop sensors required for advanced prediction algorithms in present tokamaks; to survive harsher conditions in next-step, fusion-producing devices
Control theory and application
  Design/test the compatibility and success of the coupled prediction and avoidance elements in the real-time disruption avoidance systems
Predictive analytics
  Use data, statistical algorithms and machine-learning techniques to identify the likelihood of future outcomes based on historical trends (AND physical models)

## Slide 26
This example: Greenwald limit warning during Ip rampdown
  (GWL) Greenwald limit warning issued
  (VDE) VDE condition then found 7 ms after GWL warning
  (IPR) Plasma current request not met
GWL warnings
NSTX
138854
GWL
VDE
IPR
Detected at: 0.746s
0.753s
0.753s
Disruption during
Ip ramp-down
Disruption Event Characterization And Forecasting (DECAF) code yielding initial results: disruption event chains, with quantitative warnings (2)
Event chain