## Slide 1
Ideal MHD Stability Boundaries of the PROTO-SPHERA Configuration
F. Alladio, A. Mancuso, P. Micozzi, F. Rogier*
Associazione Euratom-ENEA sulla Fusione, CR Frascati C.P. 65, Rome, Italy
*ONERA-CERT / DTIM / M2SN 2, av. Edouard Belin - BP 4025 – 31055, Toulouse, France
1

## Slide 2
2
Spherical Tokamaks allow to obtain:
• High plasma current Ip (and high <n>) with low BT
• Plasma b much higher than Conventional Tokamaks
• More compact devices
But, for a reactor/CTF extrapolation:
• No space for central solenoid (Current Drive requirement more severe)
• No neutrons shield for central stack (no superconductor/high dissipation)
Intriguing possibility ⇒ substitute central rod with Screw Pinch plasma
(ITF → Ie)
Potentially two problems solved:
• Simply connected configuration (no conductors inside)
• Ip driven by Ie (Helicity Injection from SP to ST)
Flux Core Spheromak (FCS)
Theory: Taylor & Turner, Nucl. Fusion 29, 219 (1989)
Experiment: TS-3; N. Amemiya, et al., JPSJ 63, 1552 (1993)

## Slide 3
New configuration proposed:
PROTO-SPHERA
“Flux Core Spherical Tokamak” (FCST), rather than FCS
Disk-shaped electrode driven Screw Pinch plasma (SP)
Prolated low aspect ratio ST (A=R/a≥1.2, k=b/a~2.3)
to get a Tokamak-like safety factor (q0≥1, qedge~3)
SP electrode current Ie=60 kA
ST toroidal current Ip=120÷240 kA
ST diameter Rsph=0.7 m
⇓
Stability should be improved and helicity drive may be less disruptive than in conventional Flux-Core-Spheromak
3
But Flux Core Spheromaks are:
• injected by plasma guns
• formed by ~10 kV voltage on electrodes
• high pressure prefilled
• with ST safety factor q≤1

## Slide 4
4
PROTO-SPHERA formation follows TS-3 scheme (SP kink instability)
T0
Ie=8.5 kA
Ie 8.5⇒60 kA
T3
Ip=30 kA
A=1.8
T4
Ip=60 kA
A=1.5
T5
Ip=120 kA
A=1.3
T6
Ip=180 kA
A=1.25
TF
Ip=240 kA
A=1.2
Tunnelling (ST formation)
ST compression (Ip/Ie ⇑, A ⇓ )
• Ip/Ie ratio crucial parameter
(strong energy dissipation in SP)
• MHD equilibria computed both with
monotonic (peaked pressure)
as well as
reversal safety factor profiles
(flat pressure, μ=J·B/B2 parameterized)
Some level of low n resistive instability needed
(reconnections to inject helicity from SP to ST)
but
SP+ST must be ideally stable at any time slice
⇓
Ideal MHD analisys to assess Ip/Ie & β limits

## Slide 5
5
Characteristics of the free-boundary Ideal MHD Stability code
Plasma extends to symmetry axis (R=0) | Open+Closed field lines | Degenerate |B|=0 & Standard X-points
Boozer magnetic coordinates (ξT,θ,ϕ)
joined at SP-ST interface
to guarantee ξψ continuity
Standard decomposition
inappropiate
Solution: ξψ=ξRN (N≥1); ηψ=ηB
⇓
like
ξψ( )=0 cannot be imposed
but, after degenerate X-point (|B|=0), ψT= ≠ R=0:
Fourier analysis of:
Normal Mode equation
solved by 1D finite element method
Kinetic Energy
Potential Energies

## Slide 6
6
Vacuum term computation (multiple plasma boundaries)
Vacuum contribution to potential energy not only affect T = :
contribution even to the radial mesh points ψT= and
Using the perturbed scalar magnetic potential , the vacuum contribution
is expressed as an integral over the plasma surface:
Computation method for δWv based on 2D finite element:
it take into account any stabilizing conductors
(vacuum vessel & PF coil casings)

## Slide 7
7
Stability results for time slices T3 & T4
Both times ideally stable ( >0) for n=1,2,3
(q profile monotonic & shear reversed)
Equilibrium parameters:
T3: Ip=30 kA, A=1.8(1.9), κ=2.2(2.4), q95=3.4(3.3), q0=1.2(2.1), βp=1.15 and β=22(24)%
T4: Ip=60 kA, A=1.5(1.6), κ=2.1(2.4), q95=2.9(3.1), q0=1.1(3.1), βp=0.5 and β=21(26)%
Ip/Ie=0.5
Ip/Ie=1
Oscillations on
resonant surfaces
⇓
⇓
ST
SP
ST
SP
T3
T4
n=1
n=1
ST
SP
ST
SP

## Slide 8
8
Stability results for time slices T5
Ip/Ie=2
Equilibrium parameters:
T5 (monothonic q): Ip=120 kA, A=1.3, κ=2.1, q95=2.8, q0=1.0, β=25%
T5 (reversed q): Ip=120 kA, A=1.4, κ=2.5, q95=3.5, q0=2.8, β=33%
With “reference” βp=0.3 ⇒n=1 stable, n=2 & 3 unstable
Stability restored with p=0.2
Equilibrium parameters:
T5 (monothonic q): Ip=120 kA, A=1.4, =2.2, q95=2.7, q0=1.2, =16%
T5 (reversed q): Ip=120 kA, A=1.4, =2.4, q95=2.7, q0=1.9, =18%
ST drives instability: only perturbed
motion on the ST/SP interface
Stable oscillation on the resonant q surfaces
<0
Monothonic q
Monothonic q

## Slide 9
9
Stability results for time slices T6
Ip/Ie=3
=-6.8•10-4
Reversed q
Monothonic q  n=1 stable, n=2 & 3 unstable
Equilibrium parameters:
T6: Ip=180 kA, A=1.25, κ=2.2, q95=2.6, q0=0.96, β=25%
Reversed q → n=1, n=2 & 3 unstable
Equilibrium parameters:
T6: Ip=180 kA, A=1.29, κ=2.5, q95=3.2, q0=2.3, β=33%
With “reference” βp=0.225:
Screw Pinch drives instability:
ST tilt induced by SP kink
Monothonic q → n=1,2,3 stable
Equilibrium parameters:
T6: Ip=180 kA, A=1.29, κ=2.2, q95=2.5, q0=1.12, β=15%
Reversed q → n=1,2,3 stable
Equilibrium parameters:
T6: Ip=180 kA, A=1.32, κ=2.5, q95=2.5, q0=1.83, β=19%
With “lower” βp=0.15:
Weak effect of vacuum term:
for n=1 -6.8•10-4 → -7•10-4 if PF coil casings suppressed

## Slide 10
10
Stability results for time slices TF
Ip/Ie=4
Reversed q
Screw Pinch drives instability:
ST tilt induced by SP kink
(kink more extended with respect to T6)
Monothonic q → n=1 stable, n=2 & 3 unstable
Equilibrium parameters:
TF: Ip=240 kA, A=1.22, κ=2.2, q95=2.65, q0=1.04, β=19%
Reversed q → n=1 & 2 unstable, n=3 stable
Equilibrium parameters:
TF: Ip=240 kA, A=1.24, κ=2.4, q95=2.89, q0=1.82, β=23%
With “reference” βp=0.225:
=-1.5•10-3
With “lower” βp=0.12
Monothonic q → n=1,2,3 stable
Equilibrium parameters:
TF: Ip=240 kA, A=1.24, κ=2.3, q95=2.55, q0=1.13, β=16%
With further lowered βp=0.10
Reversed q → n=1,2,3 stable
Equilibrium parameters:
TF: Ip=240 kA, A=1.26, κ=2.4, q95=2.55, q0=1.64, β=14%
Reversed shear profiles less effective in stabilizing SP kink

## Slide 11
11
Effect of ST elongation on Ip/Ie limits
=-4.4•10-2
>0
Ip/Ie=5.5
Ip/Ie=5
PROTO-SPHERA
(b/a≈3)
Stable for n=1,2,3
Equilibrium parameters:
Ip=329 kA
Ie=60 kA
A=1.23
κ=3.0
q95=2.99, q0=1.42
β=13%
(monothonic q)
Increasing κ allow for higher Ip/Ie ratio
PROTO-SPHERA
(standard b/a)
Unstable for n=1
Stable for n=2 & 3
Equilibrium parameters:
Ip=300 kA
Ie=60 kA
A=1.20
κ=2.3
q95=2.7, q0=1.15
β=15%
(monothonic q)

## Slide 12
12
Comparison with TS-3 (1)
n=1
n=1
>0
=-1.05
Ip=50 kA, Ie=40 kA
Ip/Ie~1 , A~1.8
Ip=100 kA, Ie=40 kA
Ip/Ie~2 , A~1.5
Stable q=1 resonance
Strong SP kink, ST tilt
Tokio Device had:
Simple “linear” electrodes
Oblated Spherical Torus
q<1 all over the ST (Spheromak)
Code confirms
experimental results

## Slide 13
13
Comparison with TS-3 (2)
(effect of the SP shape)
n=1
>0
Stable q=3
resonance
n=1
=-0.17
Strong SP kink,
ST tilt
If the fully stable T5 is “artificially cut”
to remove degenerate X-points
as well as disk-shaped SP
⇓
Strong n=1 instability appears,
despite higher β & q95
T5 (β=16%)
Ip=120 kA, Ie=60 kA
Ip/Ie=2 , A~1.3
T5-cut (β=16%)
Ip=120 kA, Ie=60 kA
Ip/Ie=2 , A~1.3

## Slide 14
14
Conclusions
Ideal MHD stability results for PROTO-SPHERA
•PROTO-SPHERA stable at full β 21÷26% for Ip/Ie=0.5 & 1, down to 14÷16% for Ip/Ie=4
(depending upon profiles inside the ST)
Comparison with the conventional Spherical Tokamak with central rod:
βT0=28÷29% for Ip/Ie=0.5 to βT0=72÷84% for Ip/Ie=4
•Spherical Torus dominates instabilitiy up to Ip/Ie≈3; beyond this level of Ip/Ie,
dominant instability is the SP kink (that gives rise to ST tilt motion)
• Spherical Torus elongation κ plays a key role in increasing Ip/Ie
• Comparison with TS-3 experimental results:
disk-shaped Screw Pinch plasma important for the configuration stability
Ideal MHD stability of Flux Core Spherical Torus rather insensitive to internal ST profiles
⇒ configuration quite robust from an ideal point of view
Resistive instabilities behaviour is the main experimental point of PROTO-SPHERA