## Slide 1
PROTO-SPHERA, without toroidal magnets, produces
and confines plasma tori inside magnetostatic fields
Franco Alladio, CR-ENEA Frascati, *e-mail: franco.alladio@enea.it
Crab Nebula

## Slide 2
SUMMARY
PROTO-SPHERA has produced and sustained (½ sec)
axisymmetric magnetically confined current carrying Tori
around its Plasma-Centerpost
The Plasma-Centerpost is driven by a DC voltage applied
between electrodes (DC Helicity Injection) and the Tori are formed
in presence of a pre-existing axisymmetric magnetostatic field only and in absence of any toroidal magnet
These results provides the first hints that future Fusion machines could be built using permanent magnets only

## Slide 3: wind the magnetic field in the poloidal direction to contrast particle drifts
e.g. e- → up
ions+ → down
Toroidal magnetic trap:
the inhomogeneous B
separates charges
E vertical field, through E∧B, …ejects plasma
B increases
Magnetic Confinement basics
Poloidal field drifts for particles
trapped & circulating

## Slide 4
(magneto-hydrostatic equilibrium)
flux (…also p & j ) surfaces must be Tori
Magnetic Confinement basics
A poloidal magnetic field is required to contrast particle drifts → a toroidal current has to flow in an axisymmetric plasma
Stellarators can avoid toroidal currents:
non axisymmetric magnetic coils
engender a poloidally wound field
but a price has to be payed is:
the breaking of a symmetry

## Slide 5
Cylindrical vacuum vessel geometry
has obvious advantages:
 easy to access & to repair!
Conventional Tokamak:
magnetic surfaces of toroidal plasma
surround a “Metal Centerpost”
…toroidal geometry of Vacuum vessel
PROTO-SPHERA:
magnetic surfaces of toroidal plasma
surround a “Plasma Centerpost”; slim
metal external legs current returns
…cylindrical geometry of Vacuum vessel
Main idea of PROTO-SPHERA
Electric current flow

## Slide 6
a hairy torus
can be combed
a hairy sphere cannot!
One of the “tufts” of the sphere is predominant
in expelling charged fusion products
A SPACE-THRUSTER forerunner?
Nozzle observed in PROTO-SPHERA experiment (2015)
Poincare’ “Hairy-ball theorem”: no continuous field tangent to a sphere
unless there is at least upon one point and
degenerate X-points
Last Confinement Surface spherical, but Tori inside

## Slide 7
cylindrical geometry
of Vacuum vessel ,
slim metal external legs return the current
(outside the vessel & reminiscent of a toroidal magnet in a Tokamak)
A current carrying
confined plasma Torus toroidal current IST
around a plasma Centerpost electrode current Ie
…but electrodes required inside vessel
Main idea of
PROTO-SPHERA:
degenerate
X-points

## Slide 8
The experiment now in Phase-1 is a partial set-up of the final machine
Centerpost Ie= 10 kA
…2018 Torus IST= 7 kA…!
Centerpost Ie= 60 kA
ST current IST= 240 kA
Phase-1 & Phase-2 of the experiment
Phase-1: 8 PF coils
Group-B shaping coils
Phase-2: 8 PF coils + 10 PF
Group-A compressing coils
Gas-puffed
anode
2900ºC
heated cathode

## Slide 9
Down: 3000º K heated cathode
Phase-1 (present) cathode
(54 = 18 x 3 W emitters): aim 10 kA
Phase-2 cathode, 6 x Phase-1
(324 = 108 x 3 W emitters): aim 60 kA
Up: hollow gas-puffed anode
PROTO-SPHERA Electrodes

## Slide 10
#954 Argon
The gas-puffed hollow anode
On top of the anode
degenerate X-point
acts as “plasma-nozzle”
Copper-Tungsten faces plasma
gas puffed from 100s holes
…plasma enters into holes
plasma “nozzles”
produced a metallization on anode & cathode bus-bar flanges:
Polycarbonate electrode bus-bar flanges
had to be introduced on top & bottom
#567 Argon

## Slide 11
Directly heated Phase-1 cathode only partially filled
with doubly wound Tungsten-VM filament modules
The directly heated cathode
To obtain the Plasma-Centerpost:
Cathode heated ~30 sec before the plasma,
when at 2900 ºC the Group-B-PFInt coils fired, within ~10’s ms the Centerpost power supply fired and the screw pinch plasma is produced
#954 Argon
#569 Argon

## Slide 12
#614
#977
Shaping field produced inside
the 4 cm thick Aluminum vessel
anode-to-cathode voltage
break-down ~90 V
increases up to ~200 V at 10 kA
in Argon, equatorial line-averaged electron density <ne>  Ie <ne>=4•1020 m-3 at Ie=10 kA
The Plasma-Centerpost produced in Phase-1
anode-to-cathode voltage
break-down ~320 V
decreases up to ~220 V at 10 kA
in Hydrogen, equatorial line-averaged
electron density <ne>=1.5•1020 m-3 at Ie=10 kA
The Plasma-Centerpost rotates
at ω ~ 2π (500) radians/sec
These are high-field Tokamak densities!

## Slide 13
insulator
insulator
PF4up
PF3up
PF2up
PF4low
PF2low
PF3low
anode
PF coils casings built as floating, charged by the plasma
also upper\lower extensions & lids are floating
cathode
plasma rotation: no anode-arc-anchoring
magnetic field is up\down symmetric but electrostatic field not up\down symmetric
B
E
E  B drift opposite in the anode and cathode region, but not compensated:
the top anode dominates & determines a clockwise plasma rotation (from top of machine)

## Slide 14
Taking care of electrostatic boundary conditions
2mm thick Polycarbonate linings for:
*internal Al vessel
upper diaphragm
lower diaphragm
PF2up
clearance glued
clearance glued
PF2low
*upper
insulating ring
*lower insulating
ring
2 insulating rings section
the conducting vessel
January 2018:
all these cures allowed to obtain Hydrogen plasmas
*2 Polycarbonate diaphragms glued to the internal lining
*rear of anode
*rear of cathode
*4cm thick
Polycarbonate
flanges
for bus-bars

## Slide 15
Insulating & transparent new vessel in 2019
will substitute the Aluminum vacuum vessel with a Poly methyl methacrylate (PMMA)
transparent and insulating vessel (9.5 cm thick, 2m , 1.7 m high), endowed with 20 ports
adding 2 further SS rings on top & bottom of the experiment
keeping all internal components attached to the existing SS upper\lower lid and extension

## Slide 16
from April 2018 a further Super-Capacitor power
supply feeds some of the PFExt coils
Plasma fired after 0.60 s of PF current
to allow for skin current diffusion in Al vessel
Magnetic Boundary Conditions changed
4 external PF coils added …fed in series with the Group-B-PFInt coils,
4 external PFExt (each 16 wires 25 mm2)
Hydrogen Centerpost
at full current =10 kA
seemed quite inclined
to eject a Torus
…an added vertical field
…was used as midwife!
#983, 10 kA Hydrogen

## Slide 17
Phase-2 Spherical Torus:
Phase-1 Centerpost Ie=8.5kA,
then in 1 ms up to Ie =60kA
along with increase of coil current in Group-A-PFInt
Plasma tori foreseen for Phase-2 tryed in Phase-1
4 external PFExt coils added
in 2 PFExt near equator
current flows in
opposite direction to toroidal
current inside Plasma-Centerpost
If torus forms, outward force
due to toroidal plasma current
enlarges Plasma-Centerpost
into a portion of sphere
Plasma fired after 0.60 s of PF current (skin current diffusion in Al vessel)
limits torus duration to 0.5 sec and imposes static magnetic field at torus formation

## Slide 18
If the torus does not appear, the calculated equilibrium of
Plasma-Centerpost has 2 ordinary X-points (Bpol=0) on equator
~32 cm from symmetry axis, a quite narrow Plasma-Centerpost
threshold expressible as
(rotational transform =toroidal turns of lines of force from cathode to anode)
#1098
Argon tori not obtained below Ie current threshold
Ie~3 kA
i
e
below electrode plasma current
threshold Ie~ 8.5kA narrow
Plasma-Centerpost

## Slide 19
When the current exceeds Ie ~ 8.5 kA, rotational transform of the Plasma-Centerpost
Argon Centerpost takes the shape due to the torus formation
in presence of an axisymmetric
double-null (DN) divertor
#1149 & #1160
#1160
Argon tori obtained above Ie current threshold
fitting the distance between
the 2 X-points of the divertor:
IST=5 kA in the Argon-torus
break-down ~ 200V with torus (80 without)
increases up to ~220 V at 10 kA (200 without)
Argon tori have been sustained up to 0.5 sec

## Slide 20
upper PFExt: + 8 turns•1.9 kA in series PFInt
lowest PFExt: + 8 turns•1.9 kA in series PFInt
upEquator PFExt: -8 turns•1.9 kA in series PFInt
PFExt: -8 turns•1.9 kA in series PFInt
A new Super-Capacitor power supply
(90 V, 2 kA, many sec) essential for Hydrogen Tori: Group-B-PFInt power supply was already delivering its maximal Voltage & Current,
an additional + 25% Amperes•turns were fed by Super-Capacitor
The production of Argon Tori was obtained fine tuning by -12.5% the maximum Ampere•turns of the Group-B-PFInt power supply:
=
PFExt: -4 turns•1 kA SuperCap
downEquator PFExt: -4 turns•1 kA SuperCap
The SuperCapacitor power supply allowed for H-tori

## Slide 21
#1202
#1224 10 kA Hydrogen
#1219 10 kA Hydrogen, Hα filter
Hydrogen-tori most evident shortly after the plasma break-down
or during its ramp-down
Hydrogen tori
Switching off in ~ 3 ms
5 ms after break-down, Ie reaches flat-top in ~6 msec

## Slide 22
#1219, 10 kA Hydrogen, Hα filter, but shown by cold-warm color involution
The confined toroidal current flowing inside the torus persistence longer than
the current flowing between electrodes: the torus in the last ms is kink unstable: = becomes too large
Toroidal current is confined

## Slide 23
#1202
Tori are limited by a magnetic separatrix with 2 conical divertor fans.
In Argon Hydrogen the lower (cathodic) divertor fan divertor is dominant
#1280
#1280
lower divertor with lower
polycarbonate diaphragm
(April 2018)
lower divertor with lower
AISI304 divertor plate
(July 2018)
fitting the distance between
the 2 X-points of the divertor:
IST=7 kA in the Hydrogen-torus
The dominance of the lower (cathode) divertor fan
spurious plasma current path: lower divertor -> plate -> cathode by local sparks on PF2 coil all open spaces between the PF2 and the PF3 coils will be closed

## Slide 24
#1280 with AISI340 divertor plate
break-down ~ 360V with torus (320 without)
increases up to ~ 250 V at 10 kA (220 without)
Hydrogen tori have been sustained up to 0.25 sec
(to avoid damages due to spurious plasma current)
Torus persists till anode-cathode voltage is applied
Slim tori aspect-ratio A=R/a~7
& elongation b/a=κ~3.5
…in a Tokamak could not
even be produced & sustained
R
b
a

## Slide 25
direction of in the plasma torus: opposite to direction of in equatorial PFExt coils
sign of is negative in the Plasma-Centerpost
sign of is negative as well in the plasma torus
B
j
B
B
B
j
B
B
This is a clear sign that DC Helicity Injection is in charge
of transferring plasma current from the centerpost to the torus,
just as it was imagined when the PROTO-SPHERA experiment was designed
Same sign

## Slide 26
Anode
Cathode
Magnetic
reconnection
Magnetic
reconnection
Cathode
• In front of the electrodes:
open magnetic field lines
into closed , lines
wrapped around the spherical torus
• Magnetic reconnections convert
open lines
• Open magnetic field lines are wound
in a circular direction
of Tokamaks relies on induction of PROTO-SPHERA relies on efficient but it is not forever… associated with magnetic reconnections
STEADY SUSTAINMENT OF TOROIDAL CURRENT BY RECONNECTIONS OBTAINED in 2018
PROTO-SPHERA driven by
DC currents & reconnections
Anode

## Slide 27
#1280
#1219
Reconnection bursts shake the plasma, every 2-3 ms
Visible
light
H-alpha
filter
2D approx. magnetic reconnections at ordinary X-points
3D effects: diffused (ergodic) character of the X-points

## Slide 28
Major surprise: current carrying torus formed and sustained in an external magnetostatic B *
Slow rise of currents will ease Phase-2 operations,
which will produce Spherical Tori with IST= ¼ MA
In 2019, with new insulating PMMA Vessel
substitute present impromptu PFExt coils
with larger cross-section (240 mm2) flexible cables
8+12+12+8 turns (top to bottom, flexible turn number)
fed at 2 kA by existing Super-Capacitor power supply
• will allow to form from preexisting Plasma Centerpost
Hydrogen Tori with 20 ms rise time, try and assess
differences between static and 20 ms Torus formation
from now
IST = 5-7 kA
to Phase-2
IST = ¼ MA
*A Magnetic Confinement scheme sustainable by permanent magnets?

## Slide 29
#1211
#1225
and Lop-sided-Tori,
all with visible helical components
however the plasma never disrupts
With a vertical field in slight excess (+10%) of optimal value, the Plasma-Centerpost produces odd configurations like Double-Tori
Plasma is resilient to
double & lop-sided tori
The only occurrence you should never ever consider is plasma disruption: gone for good!

## Slide 30
#1219
Metamorphosis of an hexapolar cusp into a torus
With even larger vertical fields:
the plasma exhibits an hexapolar cusp shape & a reduced current start-up: Ie<5 kA
such state can last up to 0.15 sec,
later the centerpost current reaches Ie=10 kA
and a proper Plasma-Centerpost+Torus
#1221

## Slide 31
#1221
the plasma discharge has a part with current flowing
in the Plasma-Centerpost
but the rest of the plasma
is trapped in a configuration
~axisymmetric-toroidal-cusp
#1221
proper Plasma-Centerpost + Torus
is narrower due to higher Bvert
From hexapolar cusp to compressed torus

## Slide 32
Also the poloidal field required for PROTO-SPHERA in Phase-2, for shaping and compressing the Spherical-Torus at IST=¼ MA, has an hexapolar character,
but the two electrodes are magnetically disconnected from each other
it is possible that PROTO-SPHERA in Phase-2 will form up increasing:
the Plasma-Centerpost current Ie to 60 kA & the current in the Group-A-PFInt coils
…but on a slow time scale ~20 msec
this opens the possibility of a feedback-controlled Spherical-Torus formation
Feedback-controlled Spherical-Torus formation?
field in absence of plasma IST=¼ MA plasma configuration

## Slide 33
Toroidal magnet are dispensable for producing magnetically confined tori:
a Plasma-Centerpost discharge, sustained by DC voltage electrodes, is sufficient
The tori are produced in a pre-existing axisymmetric magnetostatic poloidal field:
no variations are needed in the poloidal fields containing the plasma (virial theorem)
The confined tori are sustained until anode-to-cathode DC voltage is applied:
magnetic reconnections provide a steady-state current drive to the toroidal plasma
No disruption phenomena occur in the PROTO-SPHERA configuration:
it can produce tori at aspect ratio A=7 & elongation κ=3.5, that Tokamaks could never do
Conclusions: dispensability of toroidal magnet
& formation in magnetotatic field

## Slide 34
Magnetic reconnections are the nightmare of magnetic containment schemes …but
has a useful application of such plasma phenomena appeared in magnetic confinement?
Hopefully this will be confirmed by more powerful plasma discharges in the near future &
a vigorous self-organized plasma heating could be obtained in Phase-2 of PROTO-SPHERA,
where a total power of ~15 MW is expected to be input into the overall plasma
To assess the potential of this new configuration, Phase-2 will increase from <8% to >95%. the flux surfaces volume the torus carves from the spherically shaped Plasma-Centerpost
If the properties observed in Phase-1 will be confirmed and the energy confinement time will be long enough, this configuration could solve many issues pending in Tokamaks:
the removal of the disruption problem
the necessity of powerful plasma heating and current drive that, instead of requiring
complex external systems, will become embedded into the magnetic configuration itself
and will rely upon the spontaneous natural phenomenon of magnetic reconnections
Can magnetic reconnections be put to work?

## Slide 35
Magnetic confinement by permanent magnets?
The dispensability of toroidal magnet & the confined tori formed in a magnetostatic field
hint that magnetic confinement devices for Controlled Fusion could in principle be built using axisymmetric permanent magnets only, able to provide a poloidal magnetostatic field pre-existent to the plasma
A Plasma-Centerpost fed by two electrodes will produce and sustain the confined torus in such a poloidal field; in case the two electrodes become disconnected from each other, in terms of the pre-imposed field configuration, currents of short duration, in simply conducting coils, could be required in addition
However the currents of these coils would be gradually switched off after the plasma break-down and would vanish when the final confinement configuration, to be sustained by permanent magnets only, is achieved

## Slide 36
Metamorphosis of Tokamaks into
permanent magnet confined tori

## Slide 37
FSN Department, CR-ENEA Frascati
Franco Alladio, Paolo Micozzi, Alessandro Mancusoretired, Vincenzo Zanzaretired, Fabrizio Andreoli, Gerarda Apruzzese, Luca Boncagni, Paolo Buratti, Fabio Crescenzi, Ocleto D’Arcangelo, Edmondo Giovannozzi, Luigi Andrea Grosso, Alessandro Lampasi, Violeta Lazic, Simone Magagnino, Valerio Piergotti, Mario Pillon, Selanna Roccella, Giuliano Rocchi, Alessandro Sibio, Benedetto Tilia, Angelo Tuccillo, Onofrio Tudisco
FSN Department, CREATE Consortium and retired from CR-ENEA Frascati
Giuseppe Maffia
FSN Department, CREATE Consortium, Physics Department Università Roma-1, la Sapienza
Brunello Tirozzi
PlasmaTech Spin-off of Pisa University and Pisa University
Francesco Giammanco, Paolo Marsili
Pisa University
Danilo Giulietti
Università di Padova e Consorzio RFX and FSN Department, CR-ENEA Frascati
Giuseppe Galatola Teka, Matteo Iafrati