## Slide 1
Status of the PROTO-SPHERA Experiment – June 2019
Franco Alladio, CR-ENEA Frascati
5th ReDSoX Meeting – INAF Rome June 11th 2019
PROTO-SPHERA
Crab Nebula remnant

## Slide 2
• PROTO-SPHERA replaces the two central metal conductors of Tokamaks by a Centerpost Plasma (with helically wound B lines)
• Underlying physics is the «magnetic reconnection of a plasma». At ordinary magnetic field X-points, a «tear» is operated followed by a different «mending»; this transfers magnetic flux & electric current; magnetic field energy converts to plasma temperature
• In Phase-1 (2018) the obtained plasma tori, filled 7% of the total plasma volume. In Phase-1.5 (2019), 6 new magnetic coils are being inserted inside a new insulating vacuum chamber, the spherical tori will fill 70% of the plasma volume. Phase-2 will fill 95%: power densities ~ 100 MW/m3 ~ fission reactors
SUMMARY
2018
2.5 MW
2019
3.5 MW
2021
~20 MW

## Slide 3
Plasma current induced by
time-varying solenoid current:
flux enters from edge
plasma resistivity dissipates it
but toroidal magnet
…alone not enough…
drift of particles!
Tokamak
central
solenoid
the magnetic field winds in the poloidal direction over the magnetic surfaces to contrasts the drift of particles
First Magnetic Confinement basic tool
a toroidal field Btor
Second Magnetic Confinement basic tool
a toroidal current Itor
B increases
Itor
Btor
Btor
Axisymmetric
confinement
Equilibrium relation
creates magnetic surfaces in axisymmetry

## Slide 4
TOKAMAK:
magnetic surfaces of toroidal Plasma
surround a “Metal Centerpost”
…toroidal geometry of vacuum vessel
• PROTO-SPHERA :
…cylindrical geometry of vacuum vessel
toroidal plasma (current IST) around
a “Plasma Centerpost” (current Ie)
external metal legs as current return
PROTO-SPHERA gets rid of 1st
Magnetic Confinement basic tool!
Toroidal field , just as in a Tokamak: Ampere’s law!
…but electrodes are required inside vacuum
Electric current flowing in metal
Ie
Itor
IST

## Slide 5
Maxwell equations do not imply that a DC voltage between electrodes
can sustain a toroidal current: Magnetic Reconnections do the trick!
DC voltage from anode to cathode
SUSTAINS THE TOROIDAL CURRENT
by Magnetic Reconnections
Gas-puffed
Anode
Magnetic
reconnection
Magnetic
reconnection
PROTO-SPHERA gets rid of 2nd
Magnetic Confinement basic tool!
2900º C heated Cathode
DC voltage

## Slide 6
Tilt instability: toroidal dipole
of vertical field overturns
plasma current toroidal dipole
But PROTO-SPHERA dipoles:
“Group A” PF compression coils against Plasma dipole
“Group B” PF shaping coils aligned to Plasma dipole
Net result: rigid tilt instability is stabilized
Ideal MHD stability of PROTO-SPHERA
Stable ← → Unstable
(cutting shorter & shorter
the Plasma Centerpost
destabilizes the configuration)
ELECTRODE-FACING disk-shaped
plasma CENTERPOST PROVIDES
ideal MHD stability
PROTO-SPHERA β =1 is achievable,
faraway metal vessel is unrelevant
Stability in terms of β = plasma beta =

## Slide 7
Centerpost Ie = 10 kA
…ST current IST= 7 kA…!
Centerpost Ie = 70 kA
ST current IST= 280 kA
As built 2014, Phase-1:
8 PF coils Group-B shaping coils
Phase-2: 8 PF coils + 10 PF
Group-A compression coils
Gas-puffed
anode
2900ºC
heated cathode
Phase-1 & Phase-2 of the experiment
…as they were originally conceived (2001)
2016 Phase-1
Argon plasma

## Slide 8
#614
#977
anode-to-cathode voltage
90 V up to ~200 V at 10 kA
anode-to-cathode voltage
~320 V down to ~220 V at 10 kA
Rotating Plasma-Centerpost produced 2016-2018
DC voltage
DC voltage
Rotation ω ~ 2π (500) radians/sec
High-field Tokamak densities!
Argon, equator line-averaged electron density: <ne>  Ie <ne>=4•1020 m-3 at Ie=10 kA
Hydrogen, equator line-averaged
electron density
<ne>=1.5•1020 m-3 at Ie=10 kA
Shaping field inside
4 cm thick Aluminum vessel
January 2018:
objectives of Phase-1 achieved

## Slide 9
Phase-2 Spherical Torus:
not feasible without
internal compression coils
Plasma tori obtained & sustained during year 2018
A simpler vertical field built-up by adding 4 PFExt coils
external to the vessel
Plasma fired 0.60s after PF current (skincurrent time, 4 cm thick Al vessel)
torus duration limited to 0.5 sec → magnetostatic field at torus formation
IST
in 2 PFExt near equator
the current flows in opposite direction to
toroidal current inside the Plasma-Centerpost

## Slide 10
DC voltage
DC voltage
• An axisymmetric high density confined torus
is produced in absence of a toroidal magnet:
only external metal legs
Apart from the field due to the plasma current, driven by the DC voltage,
the overall field that confines the torus is purely magnetostatic
Major surprise: current carrying torus formed
& sustained in an external magnetostatic B field

## Slide 11
#1280 with AISI340 divertor plate
break-down ~ 360 V
at 10 kA ~ 250 V
Hydrogen tori have been sustained up to 0.25 sec
(cathode insulation was progressively degraded)
Torus persists till anode-cathode voltage is applied
Slim tori aspect-ratio A=R/a~7
& elongation b/a=κ~3.5
…unfeasible in a Tokamak!
R
b
a
DC voltage

## Slide 12
#1280
#1219
Visible
light
H-alpha
filter
2D approx. magnetic reconnections at ordinary X-points
3D effects: diffused (ergodic) character of the X-points
Reconnection bursts shake the plasma, every 2-3 ms
most compressed to most extended

## Slide 13
#1211
#1225
and Lop-sided-Tori,
With a vertical field in slight excess (+10%) of optimal value, the Plasma-Centerpost produces odd configurations like Double-Tori
Plasma is resilient to double & lop-sided tori
Large helical deformations appear,
however the plasma never “disrupts”
Disruption=plasma suddenly vanishes

## Slide 14
#1219
Hα filter
With even larger vertical fields:
the plasma exhibits an hexapolar cusp shape
& a reduced current start-up: Ie<5 kA
such state can last up to 0.15 sec
later the Centerpost current reaches Ie=10 kA
and becomes a proper Plasma-Centerpost+Torus
#1221
Hα filter
Metamorphosis of an hexapolar cusp into a torus
The Hα filtered light evidences the gas blanket around the plasma

## Slide 15
Torus formation remains to be understood
Plasma sustainment remains to be lengthened to 1 sec
New insulating PMMA Vessel
(no skin effect) Plasma Centerpost
will “slowly” form Tori (in 20 ms)
Try Torus formation from Centerpost & assess difference with magnetostatic one
Get rid of prejudice that confined plasma stability requires a metal wall nearby
the gas blanket
around the plasma
will cushion the vessel

## Slide 16
Tori as in Phase-1: Ie= 10 kA, IST= 7 kA
but formed “slowly” in ~ 20 ms
and sustained for 1 s
Will it help in understanding the
unforeseen formation dynamics?
Early Phase 1.5 Summer 2019

## Slide 17
Try Spherical Tori: Ie= 10 kA, IST= 40 kA
Phase 1.5: Autumn 2019
6 new compression coils
Red copper cable covered with Teflon
PF1
PF5
PF3.2

## Slide 18
To be built to achieve 1/3 MA Spherical Torus (Phase-2 2021)
Group A: compression coils (5+5 in series)
Electric power supplies based on Super-Caps
• Compression Group A (fit up to IST=0.5 MA)
• Cathode (Icath 10→70 kA)
• Centerpost (Ie 10→70 kA)
W cathode Filaments(54→378) (still 54 now)
PMMA Vacuum vessel
PFExt 8+12+12+8, 240 mm2
Cost incurred so far (2019) ~ 2.5 M€
Cost for completion (Phase-2) ~ 1.5 M€
Already built, for Phase 1.5, June 2019
To be built, at the end of Phase 1.5

## Slide 19
Ie = 10 kA
IST = 7 kA
Ie = 10 kA
IST = 40 kA
Ie = 70 kA
IST = 0.28 MA
end 2021
up to ~ 20 MW overall
Planned escalation of performances
2019
up to 3.5 MW overall
2018-2019
2.5 MW power to overall plasma
From 7% Torus/Sphere volume
7% of Power Input to Torus
to 70% Torus/Sphere volume
? of Power Input to Torus
From Phase-1
to Phase-1.5
to Phase-2
to 95% Torus/Sphere volume
? of Power Input to Torus
Cost 1% (β~1) of a Tokamak (β~1%), with same power input into plasma
No additional heating systems (reconnection heating)

## Slide 20
a hairy torus
can be combed
a hairy sphere cannot!
One of the “tufts” of the sphere is predominant
in expelling charged fusion products
Magnetic nozzle observed in PROTO-SPHERA experiment (2015)
Poincare’ “Hairy-ball theorem”: no continuous field tangent to a sphere
there is at least upon one point and
null or degenerate X-point
Last Confinement Surface spherical, but Tori inside
Space-thruster forerunner?

## Slide 21
Remarks:
• The machine does not aim at refining previously achieved results, but to be ground-breaking
• Until now the physics ideas seem sound: Phase-1 aims were achieved & tori were sustained
• Technically it can achieve Phase-2 without design uncertainties, with limited corrections
• Until now these corrections have dealt with boundary conditions (magnetic & electrostatic)
• The progress of the machine must follow a step by step path: no hazards, …no double steps(?)
…btw: complete successfully Phase-1.5 before moving to Phase-2 PF coils & Power Supplies
• Fusion might be a dream, but magnetic reconnections studies must aim at world excellence
…& must accommodate experiments of astrophysical interest
• Excellence in reconnection studies cannot be achieved without excellence in diagnostics
• But there’s a dream: a permanent magnets confined arc discharge as ultimate fusion machine
Francis Chen: An Indispensable Truth, How Fusion Power Can Save the Planet - Springer Science & Business Media 2011
Part II - 10 Fusion Concepts for the future - Ultimate Fusion pag. 413 …the very end of the book
One hundred years from now, what will a fusion reactor look like?
They may look like those of the Chandrasekhar–Kendall–Furth force-free configuration shown in Fig. 10.56.
The exterior regions above and below the divertor necks can be expanded like those of an axisymmetric mirror.
High-energy alpha particles leaving the divertors can be channeled into direct converters to generate high-voltage
DC directly. The central core can be slid up or down continuously to be refreshed without a shutdown.
This is a dream, but we can hope