## Slide 1
PROTO-SPHERA produces its first
Torus-&-Divertor configurations
Franco Alladio, CR-ENEA Frascati
CR-ENEA Frascati, May 28 2018
Crab Nebula

## Slide 2
List of contributors:
Paolo Micozzi, Fabrizio Andreoli, Gerarda Apruzzese, Luca Boncagni, Paolo Buratti,
Fabio Crescenzi, Giuseppe Galatola Teka , Edmondo Giovannozzi, Andrea Luigi Grosso, Matteo Iafrati, Alessandro Lampasi, Violeta Lazic , Valerio Piergotti, Mario Pillon,
Selanna Roccella, Giuliano Rocchi, Alessandro Sibio, Benedetto Tilia, Onofrio Tudisco
- ENEA
Alessandro Mancuso, Vincenzo Zanza - ENEA retired
Danilio Giulietti - Pisa University
Francesco Giammanco, Paolo Marsili - PlasmaTech Spin-off of Pisa University
Giuseppe Maffia, Brunello Tirozzi - CREATE Consortium & ENEA

## Slide 3
Outline
• PROTO-SPHERA has achieved the full Phase-1 current (10 kA) of Plasma Centerpost
• Surprise: the experiment now produces routinely Argon & Hydrogen Toroids
• DC voltage on Centerpost electrodes drives Toroidal Current (magnetic reconnections)
• How the experiment boundary conditions were modified to obtain such results
• In PROTO-SPHERA a Torus means a Divertor: this entails new modifications
• In 2019 an intermediate Phase-1½ for moving to Phase-2 on sound bases
• End of 2021: Phase-2 experiment ready to produce plasma?

## Slide 4: Wind the magnetic field in the poloidal direction to contrast particle drifts
e.g. e- → up
ions+ → down
Toroidal magnetic trap:
the inhomogeneous B
separates charges
E vertical field, through E∧B, …ejects plasma
Magnetic confinement basics
B increases

## Slide 5: → toroidal current has to flow in an axisymmetric plasma
Magnetic Confinement basics
Stellarators avoid toroidal currents:
non axisymmetric magnetic coils
engender a‘poloidally wound’field
but a price has to be payed is:
the breaking of a symmetry!
(magneto-hydrostatic equilibrium)
flux (…also p & j ) surfaces must be Tori

## Slide 6
Cylindrical vacuum vessel geometry
has obvious advantages!
 easy to access & and to repair…
“Conventional Tokamak”: magnetic surfaces of toroidal plasma surround a “Metal Centerpost”
Toroidal geometry of Vacuum vessel
PROTO-SPHERA: magnetic surfaces of toroidal plasma surround a “Plasma Centerpost”; slim metal external legs return the current
Cylindrical geometry of Vacuum vessel
…but electrodes required inside vessel
Main idea of PROTO-SPHERA
Electric current flow
No Metal Centerpost
No Toroidal Vessel

## Slide 7
In 2002 at Frascati an International Workshop advised to build the machine in 2 steps:
• Phase-1: demonstrate Plasma Centerpost’s (fear of anode arc anchoring…)
• Phase-2: machine completed such as to produce the Spherical Torus
insulator
insulator
PF4up
PF3up
PF2up
PF4low
PF2low
PF3low
cathode
anode
Also upper\lower extensions
& lids are floating
PF coils casings built as floating,
charged by the plasma
The two Phases of PROTO-SPHERA
Phase-1: 8 PFcoils
‘Group B’ shaping coils
Phase-2: 8 PF coils + 10 PF
‘Group A’ compressing coils
Centerpost Ie= 10 kA
…2018 Torus IST= 5 kA…!
Centerpost Ie= 60 kA
ST current IST= 240 kA

## Slide 8
Spheromak tilt instability is due to
dipole of containing field opposite to toroidal plasma current dipole
“Group A” PF coils (compression)
dipole moment opposes Plasma dipole
“Group B” PF coils (shaping) dipole
moment aligned to Plasma dipole
disk-shaped ELECTRODE-FACING plasma GUARANTEES ideal MHD stability
Cutting shorter & shorter
the Plasma Centerpost
PROTO-SPHERA at current
of 120 kA inside Torus
gets destabilized;
in absence of any cutting
its stability extends to current
of 240 kA inside Torus
Stable ← → Unstable
Ideal MHD stability of PROTO-SPHERA
No Spheromak

## Slide 9
Down: 3000º K heated cathode
Phase-1 (present) cathode
(54 = 18 x 3 W emitters): aim 10 kA
Phase-2 cathode, 6 x Phase-1
(324 = 108 x 3 W emitters): aim 60 kA
“Caduceus”-like W emitting spirals
have now survived > 1500 cycles
May 2015 annular
anode lowered
on top of machine
Up: hollow gas-puffed anode
Low voltage (100-350 V) between electrodes
at high-field tokamak
plasma density ~ few • 1020 m-3
PROTO-SPHERA Electrodes

## Slide 10
Switch-off of PROTO-SPHERA discharges containing a torus:
the brightness of the torus is the last to vanish,
both in the full spectrum of visible light
as well as observed trough a Balmer-alpha filter
#1219, 10 kA Hydrogen, Hα filter
#1224, 10 kA Hydrogen
Switching off in ~ 3 ms
Magnetic Confinement basics at work
Current in the Plasma Centerpost vanishes in about 3-4 ms
The energy in the Torus decays at a slower rate…

## Slide 11
During plasma switch-off the Torus current decays at a slower rate
than the Centepost current: in last ms Torus becomes unstable & kinks
(false colors)
Confining toroidal current is quite resilient
#1219, 10 kA Hydrogen, Hα filter
anode
plasma
cathode
plasma
Plasma
Centerpost
& Torus

## Slide 12
Plasma confining current inside Torus:
induced and sustained by a transformer
whose current varies in time …but there are limits: the transformer will break beyond a given current limit…
The plasma ohmic drive in a Tokamak: moving closed flux surfaces, “feeding” the plasma from outside, they are dissipated while they move toward the magnetic axis
In tokamaks this process is due to the transformer current change:
Tokamaks cannot have steady drive
…unless additional Current Drive (RF,NBI)…
Tokamak drive: AC currents, induction

## Slide 13
Anode
Cathode
Magnetic
reconnection
Magnetic
reconnection
Cathode
• Magnetic reconnections convert
open lines into closed , lines
wrapped around the spherical torus
• In front of the electrodes:
open magnetic field lines wound
in a circular direction
of Tokamaks relies on induction of PROTO-SPHERA relies on efficient but it is not forever… associated with magnetic reconnections
SUSTAINMENT OF TOROIDAL CURRENT BY RECONNECTIONS OBTAINED in 2018 & IS FOREVER!
PROTO-SPHERA current drive:
DC currents, reconnections
No RF-surfing
Current Drive
Anode

## Slide 14
PROTO-SPHERA (max 1 s plasma) aim was:
sustain Torus for 1 resistive time ~ 70 ms
PROTO-SPHERA has already sustained
a low current torus (5 kA) for ½ sec
“Air-rings” in water
Beluga
Reconnections of Jets and Tori
a common occurrence in Nature!
Plasma examples: Solar Flares
Magnetic Reconnections, Coronal Heating
Etna Volcano
“Smoke-rings”
in air
Hydrodynamics
examples

## Slide 15
Similar short duration configurations (1-10 µs) obtained by the Plasma Focus
The simply connected spherical-torus configuration
as observed by a streak-camera on a plasma focus
invented by N. Filippov in the ‘60s
PROTO-SPHERA precursor: the Dense Plasma Focus

## Slide 16
60 µs formation
20 µs sustainment
total duration 80 µs ∼ 100 τAlfvén (short but significant…)
TS-3 (Tokyo University): plasma toroids magnetic reconnection around a metal centerpost
In 1993 TS-3 removed the metal centerpost, applied 1kV between
two plasma guns, produced a Ie = 40 kA Plasma Centerpost
non-linear “kink” instability formed a Spherical Torus
toroidal plasma current 50 kA < IST < 100 kA
PROTO-SPHERA: TS-3, the Japanese precursor

## Slide 17
Breakdown in small spaces, with extremely high filling pressures and 10 kV voltages
Impulsive formation, Spheromak accelerated and expanded into a flux conserver
PROTO-SPHERA vs GUN-INJECTED FLUX-CORE-SPHEROMAKS
PROTO-SPHERA ISN’T A FLUX-CORE-SPHEROMAK
PROTO-SPHERA
TS-3
• Designed for a Tokamak-like field-line
rotational trasform (q0 ≥ 1, qedge~ 3)
aspect ratio A = R/a ≥ 1.2
elongation k = b/a ~ 2.3
• Plasma Centerpost in front of
electrodes is mushroom-shaped
• At low voltage (<< 1 kV), inside big vessel
• PROTO-SPHERA static formation

## Slide 18
Axisymmetric simulation of Torus formation
Non-axisymmetric simulation of Torus formation
Resistive MHD simulations by Ricardo Farengo (ISTW2008-Frascati)
Formation time scale (τAlfvén•τResist)1/2 ~ 0.6 ms (τAlfvén ~ 0.5 μs, τResist ~ 70 ms)
PROTO-SPHERA Torus formation:
Centerpost current Ie= 60 kA
ST toroidal current IST= 240 kA
ST diameter 2Rsph= 0.7 m
…2018 Experiments
show that Torus forms
with static B field !
No Spheromak

## Slide 19
a hairy torus
can be combed
a hairy sphere cannot!
Predominantly one of the “tufts” of the sphere:
expels charged fusion products
A SPACE-THRUSTER forerunner?
Nozzle observed in PROTO-SPHERA experiment (2015)
Poincare’ “Hairy-ball theorem”: no continuous field tangent to a sphere
unless there is at least upon one point and
Last Confinement surface can be a sphere, but contains Tori

## Slide 20
  Polycarbonate (transparent) anode bus-bar flange on top & bottom of machine
Heavily metallized
top & bottom bus-bar flanges
2015/16 experiments produced a heavy metallization on top
(anode) & bottom (cathode) bus-bar vacuum entrance flanges,
associated with magnetic “nozzles”
Electrostatic plasma effects: taking care of boundary conditions
inserted in December 2016
Light of Argon discharges through bus-bar flanges on top & bottom of machine

## Slide 21
2mm thick Polycarbonate lining covers Al vacuum vessel
inserted in
December 2016
2mm thick
Polycarbonate
screens
surround
rear of
anode
&
rear of
cathode
inserted in December 2017
upper insulating ring
lower insulating ring
inserted in May 2017
Electrostatic plasma effects: taking care of boundary conditions

## Slide 22
November 2017: the narrow clearance has been closed by a bonding material able to sustain the diaphragms weight
To avoid the flow of plasma currents outside the centerpost two large insulating polycarbonate diaphragms were inserted
May 2017
upper diaphragm
lower diaphragm
PF2up
1-2 mm clearance
1-2 mm clearance
January 2018:
all these cures allowed to obtain Hydrogen plasmas
Electrostatic plasma effects:
care for boundary conditions
PF2low

## Slide 23
Insulating & transparent new vessel being built for Phase-2
will substitute the Aluminum vacuum vessel with a Polymetacrylate (PMMA)
transparent and insulating vessel (9.5 cm thick, 2m , 1.7 m high), endowed with 20 ports
adding 2 further SS rings on top & bottom of the experiment,
keeping all internal components attached to the existing SS upper\lower lid and extension

## Slide 24
Plasma rotation in Tokamaks
always stabilizes the plasma
best way of injecting fuel is
from inboard (high field side)
#977, 10 kA Hydrogen
break-down Ve ~ 320 V, steady Ve ~ 220 V
#614, 8.5 kA Argon
break-down Ve ~ 90 V, steady Ve ~ 200 V
PROTO-SPHERA Plasma Centerpost rotates
& therefore avoids anode arc-anchoring
(Pisa University & its PlasmaTech spin-off) line-averaged electron density on plasma equator:
in Argon Centerpost <ne> ~ Ie
at Ie =10 kA, <ne> ~ 4•1020 m-3
in Hydrogen Centerpost
at Ie =10 kA, <ne> ~ 1.5•1020 m-3
Anode arc-anchoring means
that a plasma arc discharge
is localized on an anode spot

## Slide 25
Lines: magnetic field Color contours: electrostatic potential, Arrows: E field
No Anode-Arc Anchoring: Electrostatic plasma effects!
plasma rotation does the trick!
VPF4up ~ +95 V
Vanode ~ +139 V
VPF2-3up ~ + 50 V
VPF2-3low ~ -12 V
Vcathode ~ -80 V
VPF4low ~ -41 V
GND
#974 10kA Hydrogen
magnetic field is up\down symmetric but electrostatic field not up\down symmetric
VLidUp ~ +95 V
VLidDown ~ -56 V

## Slide 26
from April 2018 a further Super-Capacitor power
supply feeds some of the PFExt coils
Plasma fired after 0.75 s of PF current
to allow for skin current diffusion in Al vessel
“Magnetic Boundary Conditions” changed
4 external PF coils added …fed in series with the internal PFInt coils,
4 external PFExt (each 16 wires 25 mm2)
Hydrogen Centerpost
at full current =10 kA
seemed quite inclined
to eject a Torus
…an added vertical field
…was used as midwife!
#983, 10 kA Hydrogen

## Slide 27
In absence of Torus formation
With Torus formation
Ie= 3 kA
Ie= 5 kA
Ie= 10 kA
ITorus= 5 kA
Torus forms at the expected current: Ie ~ 8 kA
#1098, Argon
#1096, Argon
#1091, Argon
March 2018 Torus formed in Argon plasmas

## Slide 28
#1149, Argon
#1160, Argon
The “gentle Divertor” of the (barely visible) Argon Torus
lower Divertor fan is dominant & slightly shifts down the Torus

## Slide 29
The Argon Torus has been sustained for up to ½ sec
#1160, Argon, X-points fit IST=5 kA
Argon Torus
break-down Ve ~ 200 V
steady Ve ~ 220 V

## Slide 30
evident at plasma breakdown & …after ¼ sec at plasma switch-off
April 2018 Torus formed in Hydrogen Plasma
#1202, Hydrogen
Hydrogen Torus
break-down
Ve ~ 360 V
steady Ve ~ 320 V

## Slide 31
#1195, Hydrogen, ~22 ms long movie
#1221, Hydrogen, Hα filter, ~22 ms long movie
Confining toroidal current injected in pulses every 2-3 ms
Identified as magnetic reconnections: every pulse ejects plasma along the Divertor fans
Argon plasma Torus much less visible, but ejection along fans every 2-3 ms very evident

## Slide 32
The “uncouth Divertor”
of the Hydrogen Torus:
lower divertor fan strongly dominant
spurious current path below diaphragm
The present divertor plate is the lower polycarbonate
diaphragm: an unsuitable choice of material!
But when we put it inside PROTO-SPHERA
we did not expect to be able to form a Torus!
A new lower metal diaphragm being built now;
in 2019 PROTO-SPHERA will have 2 suitable plates
#1202, Hydrogen. ¼ s full movie

## Slide 33
Reconnections, Helical States & Double Tori
#1211
Hydrogen
#1225
Hydrogen
Vertical field in eccess? …Double Torus! …or Helical States …or lop-sided Tori!
The only occurrence you should never ever consider is plasma disruption: gone for good!

## Slide 34
#1219, Hydrogen. ¼ s full movie, Hα light saturates
#1221, Hydrogen. ¼ s full movie, Hα light
Disruptions do not exist, even if plasma does crazy movements, it never vanishes
It can well recover from Multiple Tori, Helical States, Lop-sided Tori
Disruptions gone for good!

## Slide 35
upper PFExt 8 turns•1.9 kA in series PFInt
lowest PFExt 4 turns•1.9 kA in series PFInt
upEquator PFExt 8 turns•1.9 kA in series PFInt
PFExt 8 turns•1.9 kA in series PFInt
up/down dissymmetric PFExt contrasts divertor dissymmetry
The new Super-Capacitor power supply
(90 V, 2 kA, many sec) has been essential for Hydrogen Tori: the Internal PF power supply was already delivering its maximal Voltage & Current, an additional +25% Amperes•turns were fed by Super-Capacitor
The production of Argon Tori was obtained fine tuning by -12.5% the maximum Ampere•turns of the Internal PF power supply:
Ar Tori ~ 5 kA, H Tori ~ 7 kA
PFExt 4 turns•1 kA SuperCap
downEquator PFExt 4 turns•1 kA SuperCap

## Slide 36
Major surprise: Torus forms in a static field
the plasma operations will be easier in Phase-2,
which will produce Spherical Tori with IST= ¼ MA
In 2019, Phase-1½ ( new insulating PMMA Vessel)
substitute present impromptu PFExt coils
with larger cross-section (240 mm2) flexible cables
8+12+12+8 turns (top to bottom, flexible turn number)
fed at 2 kA by existing Super-Capacitor power supply
• will allow to form from preexisting Plasma Centerpost
Hydrogen Tori with 20 ms rise time, try and assess
differences between static and 20 ms Torus formation
• will allow to switch from DN to SN Divertor configurations
from now
IST = 5-7 kA
to Phase-2
IST = ¼ MA
No Spheromak

## Slide 37
What remains to be built to achieve a ¼ MA Spherical Torus (2021?):
Group A: compression coils (5+5 in series)
cost ~ 0.5 M€
Electric power supplies:
1) Group A cost ~ 0.1 M€
2) Cathode (Icath 10→60 kA) cost ~ 0.2 M€
3) Centerpost.(Ie 10→60 kA) cost ~ 0.6 M€
Super-Capacitors will be used
W cathode Filaments1(54→324) cost ~ 0.1 M€
Cost incurred so far ~ 2.0 M€
Cost for completion ~ 2.0 M€
PMMA Vacuum vessel1 cost ~ 0.2 M€
including vacuum components, divertor plates
1, 1 Under construction, * to be built before 2019
PFExt* 8+12+12+8, 240 mm2 each cost ~ 40 k€

## Slide 38
PROTO-SPHERA will not need additional heating…?
…magnetic reconnections heat the Solar Corona!
Phase-2 power injected into plasma > 250 V • 60 kA = 15 MW …how much into Torus?
~ 0 MW, T = 10 eV
“cold” plasma:
divertor studies
< 1 MW, T = 100 eV
“lukewarm”plasma:
magnetic reconnection
studies at S ~ 104
a few MW, T =1 keV, “hot” plasma at β ~ 1, no disruptions
no additional heating & no current drive required,
same T as a Tokamak, but 1/100 of the cost!
Fritz Lang’s Metropolis (1926)

## Slide 39
Perspectives
PROTO-SPHERA will assess a new magnetic confinement configuration:
• simply connected (easy to build, maintain & modify)
• sustained (indefinitely) by magnetic reconnections induced by DC voltage
• mixed magnetic & electrostatic confinement, plasma flow being paramount
• could provide laboratory examples and insight into cosmic reconnection phenomena
• (if high T from magnetic reconnections) plasma β ~ 1: small size future Fusion reactor?
• a forerunner for a (far future) Fusion Space Thruster?
Proto-Sphera can pursue such an aggressive program:
with limited costs ( ~ 2.0 M€ ); with flexibility (new components easy to accommodate)
。。。放龙如海! fànglóng rùhǎi!
…let the Dragon swim in open sea!

## Slide 40
+ Other
authors