## Slide 1: 3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment Annamaria Pau1, Shayesteh Naghinajad1, Franco Alladio2, Paolo Micozzi2, Luca Boncagni2 1Department of Structural and Geotechnical Engineering, Sapienza University of Rome, Italy 2NUC Nuclear Department, ENEA, Frascati, Italy
ASME QNDE
51st Annual Review of Progress in
Quantitative Nondestructive Evaluation
Denver, CO, USA
July 22-24 2024

## Slide 2
Computed Tomography
Computed Tomography (CT) is the process of imaging a cross-section of some solid - Greek tomos - slice. It enables seeing through objects instead of making real cuts, therefore it has important applications in the medical field and in nondestructive structural monitoring.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024
Notes: First of all, I would like to introduce you to the concept of CT

## Slide 3
Computed Tomography
CT scanning involves the solution of an inverse problem which can be formulated as:
based on the knowledge of some data called projections, determine the distribution of some physical property.
The fact that this problem admits a unique solution was demonstrated back in 1917 by the mathematician Johann Radon. Projections can be obtained with whatever signal that interacts with the material we aim to scan and can be X-rays, ultrasounds, GPR, that is presently in use in civil and industrial applications to assess the distribution of rebars of reinforced concrete.
Picture taken from Alani et al. The use of ground penetrating radar and microwave tomography for the detection of decay and cavities in tree trunks, Remote Sensing, 2019
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 4
2D Computed Tomography – Radon Transform
Analytical algorithms for CT are based on the concept of projection.
The mathematician Johann Radon in 1917 was the first to demonstrate the possibility to reconstruct the shape of an object based on its projections.
The projection of a plane object onto a line is nothing but the line integral of some transmitted dynamic response quantity following some emission which ''illuminates'' the object. A projection is a sort of shade which an object projects onto a line.
The line integral of a density function f(x,y) over the line at a distance t from the origin and inclined by an angle q is: t
d Dirac delta
is a projection of the density function onto the
line inclined by q
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 5
The collection of all the projections in the (x,y) plane is the 2D Radon Transform of the function f(x,y)
2D Radon Transform
We are moving from a representation in the Cartesian plane (x,y) to a representation in the plane (t,q).
scan 1
scan 2
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 6
6
=1 in the circle
=0 elsewhere
2D Radon Transform - Example
Source image
Radon Transform
Using the Dirac delta
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 7
The Fourier Slice theorem is key to image reconstruction: it proves that the Fourier Transform of a projection of the density function (a column of the Discrete Radon Transform) is a slice of the 2D Fourier transform of the image.
Proof:
The Fourier Slice Theorem – 2D
Projection
Then, the image can be reconstructed by simply taking the 2D inverse Fourier Transform of the Fourier Transforms of all the projections!
FT of the Projection
w is the wavenumber
Convert in the original coordinate system
But this is the 2D FT at spatial frequencies
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 8
IQ=99%
IQ=98%
The Fourier Slice Theorem
However, things are not as easy as they might look like at a first sight. In fact, when we calculate the 2D Inverse Fourier Tranform of the following function
We have a grid (red) of values where the function is known that does not match the regular grid of values where the function is needed for inversion (blue). An interpolation is done, zeros are placed where interpolation is not possible.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 9
α = (cosθcosϕ, sinθcosϕ, sinϕ)
Eq.8
3D Radon Transform
A similar procedure can be implemented in 3D.
Definition of the 3D Projection of a density function onto a plane:
The lines onto which the integration is carried out are orthogonal to the versor
And define the normal to a plane. The set of all the projections for all the angles q and f is the 3D Radon transform of the density function f(x,y,z).
The procedure can be implemented also for cylindrical projections. In this case the normal to the projection lines
will be described by one angle only:
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 10
3D Fourier Slice Theorem
We formulated a corollary of the Fourier Slice Theorem which proves that the 2D Fourier transform of a plane projection of the density function is a plane slice of its 3D Fourier transform.
Proof:
Projection
2D FT of the Projection m and n are the wavenumbers
Convert back to the original coordinate system
But this is the 3D FT with wavenumbers
To reconstruct f(x,y,z) we have to calculate the 3D inverse Fourier transform of the collections of 2D Fourier transforms of its projections onto planes.
Also in the 3D case there are the sampling problems we have in the 2D case, which are dealt with interpolation.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 11
The projections are spherical projections and identified by two angles.
Here are some examples.
Image reconstruction in 3D faces similar problems as in 2D, i.e., blurring due to the reduced number of projections, and the need to interpolate on a regular grid of wavenumbers.
3D Image Reconstruction
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 12
PROTO-SPHERA is a magnetic confinement plasma experiment for Controlled Thermonuclear Fusion research, whose aim is to form a spherical plasma torus not around a metal centerpost (as in Tokamaks), but around a plasma centerpost. The vessel is simply connected, different from the structure of Tokamaks.
It exploits the self-organization of plasma following the application of a difference of potential between two electrodes, connected by eight copper bars which close the circuit, and some internal poloidal coils (magnets).
PROTO-SPHERA experiment at ENRA Frascati laboratories
Schematic of PROTO-SPHERA setup
Application: 3D reconstruction of light emission density in PROTO-SPHERA
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024
Notes: PROTOSPHERA DOES NOT ACTUALLY DO NUCLEAR FUSION, which would require using isotopes like Deuterium or Tritium instead of stable gases like Hydrogen, Helium or Argon. But it is propedeutical to the nuclear fusion, which could be realized with a larger vessel and unstable isotopes.

## Slide 13
3D representation of the vessel with the cameras positions
and their view lines b) Up view of the configuration
An ultra fast camera, with a resolution of 1024x1024 pixels and 3600 fps
six fast cameras, with a resolution of 640x480 pixels and 600 fps: the pictures captured by these six cameras are assumed to be the plane projections of the light emission density.
Langmiur probe, which measures the electron density
3D representation of the vessel with camera positions l
Upper view of the configuration
Tomographic diagnostic
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 14
Sample of 3D Tomographic image reconstruction
Helium
Hydrogen
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 15
Self-organization of magnetically-confined plasma
8 ms
Once obtained the light emission density, the solid can be cross-sectioned by vertical planes and the same phenomena observed.
This sequence of reconstructed light emission densities enables to disclose the mechanism of self-organization of plasma. Based on magneto-hydrodynamic models, it was expected that, first, a plasma column (pinch or centerpost) is formed at low current. Then, when the current is increased, the magnetic field lines bend, and the pinch becomes unstable, which gives rise to the formation of the torus around the centerpost.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 16
Self-organization of magnetically-confined plasma
Or by horizontal planes, providing proof of the existence of the torus.
Shayesteh Naghinajad 3D tomography for non-destructive structural inspection and image reconstruction,
PhD Thesis (2024)
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 17
Animations
The torus has fluctuating intensity in Helium shot 2141.
.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 18
the outermost part of the central pinch.
X
Helium 0.25m
Hydrogen 0.23m
Measurement of the thickness of the torus
Horizontal cross-sections.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 19
The 3D tomography enabled disclosing the inner green and blue colors (likely tied to higher temperatures), which were hidden by the strong golden brilliance of the "ionization peel" existing between the plasma and the gas cushion that surrounds it.
Vertical cross-sections
Energy 20-30 eV
Langmiur probe
It corresponds to
200 000 °C
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 20
the outermost part of the central pinch.
X
X-points are points where the poloidal component of the magnetic field has zero magnitude. They are likely associated with minimum light emission. They can be identified as zeros of the diagonal of the Jacobian of the emission density function:
X-points in vertical cross-sections
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 21
Inclined vertical cross section of Helium shot 2141. The plasma self-organization is extremely similar to some astrophysical arrangement of plasma in pulsars.
Animation of a vertical cross section
Chandra X-ray observatory Crab nebula, NASA picture
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024
F. Alladio, P. Micozzi, L. Boncagni, A. Pau, S. Naghinajad, S. Macera, Y. Damizia, P. Buratti, F. Filippi, G. Galatola Teka, F. Giammanco, E. Giovannozzi, M. Iafrati, A. Lampasi, P. Marsili, PROTO-SPHERA: a magnetic confinement experiment which emulates the jet + torus astrophysical plasmas, Plasma Physics and Controlled Fusion vol. 66(3), 035011, 2024

## Slide 22
Conclusions
An imaging technique based on the formulation of the Fourier slice theorem in 3D is applied to the reconstruction of distribution of light emission of magnetically confined plasma in 3D.
The algorithm is applied to data representing the visible light emission of Hydrogen and Helium plasma, recorded by six high-resolution cameras within the framework of the PROTO-SPHERA experiment, carried out at the ENEA Frascati laboratories.
We have shown that six pictures captured by cameras arranged in cylindrical symmetry enable a meaningful 3D reconstruction of the plasma spatial distribution of the PROTO-SPHERA experiment at different time instants.
It was shown how the plasma torus grows in around 8 ms from a kinked filament, due to the destabilization of the plasma centerpost. The availability of the spatial distribution of light emission enables carrying out cross sections of the plasma: these sections pointed out the presence of a green light emission from the core of the plasma, which was hidden
by the external golden ionized peel. Moreover, equatorial cross-sections enabled the measurement of the thickness of the torus, which resulted to be between 0.25 and 0.35 m.
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024

## Slide 23
Thank you for listening
3D Tomography of Hydrogen and Helium plasma produced in the PROTO-SPHERA experiment
Pau, Naghinajad, Alladio, Micozzi, Boncagni – QNDE, Denver, USA, 22-24 July 2024