## Slide 1
First results and perspectives
of the PROTO-SPHERA experiment
P. Micozzi1, F. Alladio, L. Boncagni, F. Causa, E. Giovannozzi, A. Grosso, A. Lampasi,
G. Maffia, A. Mancusoretired, V. Piergotti, G. Rocchi, A. Sibio, B. Tilia, V. Zanzaretired
Centro Ricerche ENEA, Frascati C.P. 65, Rome, Italy 1e-mail: paolo.micozzi@enea.it

## Slide 2
2
Spherical Tokamaks allow to obtain:
High plasma current Ip with low BT, high β
and more compact devices
But, for a reactor/CTF extrapolation:
• No space for central solenoid (Current Drive requirement more severe)
• No neutrons shield for central stack (no superconductor/high dissipation)
Intriguing possibility ⇒ substitute central rod with Screw Pinch plasma
Potentially two problems solved:
• Simply connected configuration (no conductors inside)
• Ip driven by Ie (Helicity Injection from SP to ST)
Flux Core Spheromak (FCS)
Theory: Taylor & Turner, Nucl. Fusion 29, 219 (1989)
Experiment: TS-3; N. Amemiya, et al., JPSJ 63, 1552 (1993)
(ITF → Ie)

## Slide 3
3
New configuration proposed
(Alladio F. et al. 2006 Nucl. Fusion 46 S613):
PROTO-SPHERA
“Flux Core Spherical Tokamak” (FCST), rather than FCS
Disk-shaped electrode driven Screw Pinch plasma (SP)
Prolated low aspect ratio ST (A=R/a≥1.2, κ=b/a~2.3)
to get a Tokamak-like safety factor (q0≥1, qedge~3)
SP electrode current Ie=60 kA
ST toroidal current Ip=120÷240 kA
ST diameter Rsph=0.7 m
⇓
Stability should be improved and helicity drive may be less disruptive than in conventional Flux-Core-Spheromak
But Flux Core Spheromaks are:
• injected by plasma guns
• formed by ~10 kV voltage on electrodes
• high pressure prefilled
• with ST safety factor q≤1

## Slide 4
4
PROTO-SPHERA formation follows TS-3 scheme (SP kink instability)
T0
Ie=8.5 kA
Ie 8.5→60 kA
T3
Ip=30 kA
A=1.8
T4
Ip=60 kA
A=1.5
T5
Ip=120 kA
A=1.3
T6
Ip=180 kA
A=1.25
TF
Ip=240 kA
A=1.2
Tunneling (ST formation)
ST compression (Ip/Ie↑, A ↓ )
Smoke-ring-like formation
Formation time scale:
Alfvén MHD growth time τA~ 0.5 μs
Resistive diffusion time τR~ 70 ms
(τRτA)1/2~ 0.6 ms for IST=120 kA (2xIe)
Garcia-Farengo, PoP 16,112508 (2009)
Farengo, ISTW2008 - Frascati

## Slide 5
5
Smoke-ring-like formation
• Stable Screw Pinch formed at Tokamak pressures
(10-3÷10-2 mbar) & with low voltage break-down (100-200 V)
• Ip/Ie ratio relevant parameter
(strong energy dissipation in SP)
• MHD equilibria computed both with
monotonicas well as reversal safety factor profiles
⇓
magnetic configuration is quite robust
Some level of low n resistive instability needed
(reconnections to inject helicity from SP to ST)
but
SP+ST must be ideally stable at any time slice
⇓
Ideal MHD analysis to assess Ip/Ie & β limits
(Micozzi P. et al., 2010 Nucl. Fusion 50 095004)
⇓
Key points of proto-sphera design
For low toroidal numbers n=1, 2 & 3
ideal MHD stability obtained
expressed with
up to β = 21÷26% , IST/Ie= 0.5-1
up to β = 14÷15% , IST/Ie= 2-4
expressed with
up to βT0=28÷29% , IST/Ie= 0.5-1
up to βT0=72÷84% , IST/Ie= 2-4
Examples of n=1&2
instabilities at high β

## Slide 6
6
Smoke-ring-like formation
“Smoke-ring like
self-organization”
Anode
Cathode
Etna volcano
Beluga
Crab Nebula
William Irvine-University of Chicago
Helicity injection to sustain the plasma torus:
driven relaxation of Plasma Central Column forms & sustains the ST
• IST= 240 kA (4xIe) really achievable?
• Can it be sustained by H.I. for at least τR~ 70 ms?
• Resistive MHD stability & confinement?
Critical points of PROTO-SPHERA
magnetized configuration
produced by Supernova explosion

## Slide 7
7
PROTO-SPHERA was built (2006-2009) by ASG Superconductors of Genoa, cost 1 M€
Cylindrical vacuum vessel was START vacuum vessel, donated by Culham in 2004
Culham …to Frascati the old vacuum vessel found its way…
Years 2004 - 2010:
…from ideas …to detailed design …to hard metal

## Slide 8
8
Proto-Sphera Phase-2
Aims: ST formation, compression & sustainment
(All parts will be reused)
By adding:
5 pair of new PF coils
New power supplies
Full amount of Tungsten wires (324 Vs 54) on the directly heated cathode
now only partially filled
8 PF coils
Centerpost only
8 + 10 PF coils
Proto-Sphera Phase-1
Aims:
1) Breakdown
2) Stable formation of plasma ‘mushrooms’
3) Stable (≈1 s) achievement of Ie = 8.5 kA

## Slide 9
9
The poloidal field (PF) coils designed as two sets each connected in series
Group B (4+4 coils): Centerpost shaping PF coils …thick AISI casings (τ~2ms), now inside machine
Group A (5+5 coils): Spherical Torus compression PF coils …not yet built
 High voltage (∼20 kV) insulation: fast current increase (0.5 ms)
Thin Inconel casings to allow for B diffusion in τ~200 µs across them
…waveform of Group A
current provides ohmic
drive to torus up to 120 kA
Paradigm reversal:
ohmic drive followed
by Helicity Injection
To fire the plasma centerpost
3 Power supplies have been built
• Cathode heating 6 x(1.7 kA,25 V)rms
• PF coils: 2kA, 350 V
• Plasma centerpost: 10 kA, 350 V
(cost 700 k€)
ASG 2007 Genova
ASG 2009

## Slide 10
10
annular anode
(gas puffed)
Only the PF coils necessary for setting up the plasma centerpost have been built
PF4low
PF2low
PF3low
anode
plasma current must run
through both PF2 throttles
8 PF coils in series
inside the machine
Aluminium cylindrical
START vessel
Stainless steel up\down
new extensions
Stainless steel up\down new lids
vacuum vessel is GND potential
PF coils casings built as floating, can be connected to potentials: anode +, cathode -, vessel 0
cathode
PF3up
PF2up
annular cathode
PF4up

## Slide 11
11
Being afraid of anode attachment, often observed in arc discharges
(arc welding, plasma torches)
the first rounds of experiments
had a simple cylindrical anode
break-down was easily achieved,
apart from this the cylindrical anode was just a source of troubles
April 2015: annular anode installed
2015 annular anode
2014 cylindrical anode
Cylindrical cathode results
break-down 170 V +10 ms, 500 A +20 ms, 1.5 kA
Anode camera
Centepost camera

## Slide 12
12
Centepost camera
up: hollow gas-puffed anode
down: 3000°K heated cathode
present stage cathode
(18 x 3 emitters): aim 10 kA
final stage cathode, 6 x present
(108 x 3 emitters): aim 60 kA
Emitting W spirals up to now survived ~ 1000 cycles
May 2015
Annular anode lowered on top of machine

## Slide 13
13
Centepost camera
Argon plasma: break-down 80 V
hollow annular anode performs
• plasma goes through both PF2 throttles
• plasma enters anode gas-puffing holes
• no sign (I < 3.5 kA) of anode attachment
• filling pressure 10-3 - 10-2 mbar
annular anode plasma is never filamented
anode
camera
cathode
camera
Good surprise!
Cathode
plasma
filaments
disappear
going
towards
anode
whereas annular cathode plasma (sparse emitters)
and even plasma centerpost are filamented

## Slide 14
14
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
VPF4up ~ 0 V
Vanode ~ +45 V
VPF2-3up ~ +25 V
Vvessel = 0 V (ground)
VPF2-3low ~ 0 V
Vcathode ~ -35 V
VPF4low ~ -15 V
PF2\3low to GND (1 Ω)\PF4low cathode (0.5 Ω)
PF2\3up to anode (1 Ω)\PF4up cathode (10 Ω)
distribution of electric potential is not up-down symmetric: near both anode and cathode the uppermost PF coil casings is at GND
vacuum vessel at GND
PF coil casings can either be
at floating potential or can be connected to:
anode +, cathode -, vessel 0
through ~ 1 Ω resistors
but the electric potential distribution is dominated by the plasma
Electrostatic plasma effects

## Slide 15
15
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
self-organization at work inside
annular electrodes plasma…
Plasma-induced electric potential
near the annular anode:
E-field is perpendicular to B-field
…E ∧ B azimuthal plasma rotation
…starting from PF2up throttle
Plasma-induced electric potential
near the annular cathode:
E-field is parallel to B-field
…no E ∧ B plasma rotation
vE∧B=(E/B) ~ 104 m/s ~ vdrift ~ vthi

## Slide 16
16
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
May 2015 annular anode experiment
half of the plasma current: (1kA\2kA)
was going around the required path due to
equatorial X-point inside the vessel
Argon plasma
Hydrogen plasma
discharges along field lines near X-point
Shot 78

## Slide 17
17
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
The equatorial X–point has been removed from inside the vessel
4 external PF coils have been added (home-made from spare connection cables)
…and fed in series with the internal PF coils (PF coils power supply has sufficient margin)
plasma fired after 0.75 s of PF current to allow for skin current diffusion in Al vessel and SS lids
4 additional external PF coils

## Slide 18
18
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
October 2015 experiments with external PF:
Argon discharge reaching 3 kA for 0.15 s
the whole plasma current runs through both PF2 throttles
plasma fired after 0.75 s of PF current
(skin current time to remove X-point from inside vessel)
Shot 205

## Slide 19
19
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
~ 1.5 kA lost
from main plasma
in discharge from
cathode down to
lid\vessel
Argon plasma
aiming to 4 kA
reaches 3.5 kA
10 V spikes appearing on floating voltages on lower PF coils
are associated with plasma current outer path
plasma current
lost on both
PF2 throttles
Plasma current outer paths for I > 3 kA
Shot 208

## Slide 20
20
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
when plasma current takes outer path cathode seems less emitting
plasma current 3.5 kA
plasma current 2 kA, 1.5 kA lost
Magnetic tailoring in order to have a better filling of electrodes
current flows only in external PF near equator
Shot 227
Shot 208

## Slide 21
21
Centepost camera
Cathode
plasma
filaments
disappear
going
towards
anode
voltage spikes have been eliminated on PF2/3low,
after 1 V amplitude jump even small sparks vanish
voltage jump does not lose plasma current
very quiet plasma at 2 kA after voltage jump
Straighter grounding of lower PF coils and better filling of cathode
flowing current only in the two external PF coils nearer to equator
Argon discharge at 2 kA
Shot 227

## Slide 22
Group A: ST compression coils (5+5 series)
Not yet built, but inner vessel ready to host
• high voltage (~20 kV) insulation
thin Inconel casings cost ~ 0.5M€
Final Power Supplies for:
1) Group A PF coils cost ~ 0.1M€
2) Cathode (Icath 10 → 60 kA) cost ~ 0.2M€
3) Screw Pinch (Ie 10 → 60 kA) cost ~ 0.6M€
SuperCapacitors will be used
To be build after 10 kA
plasma centerpost achieved
• Spherical Torus Compression PF Coils
• 324 W filaments (full filling of cathode)
• Final Power supplies
Tungsten filaments (54 → 324)
Replica of existing (all replaced) cost ~ 0.2M€
Cost up to now ~2.0 M€
Cost for final stage of experiment ~1.6 M€
22

## Slide 23
Proto-Sphera power supplies: Supercapacitors will be used
Phase-1
Maxwel Technologies SC
(C=63 F , V=125 V)
Advantages:
 No connection to 20 kV substation and no step-down transformers
 Standard SCR Controller
(no thyristor bridges)
 Very reduced cost!
For the “PF coils A” P.S. a small
conventional capacitor bank (Ducati) must be added
Cost ≈ 0.6M$
Cost: less than 0.1M$
Screw Pinch
PF coils ‘A’
qPinch=0.45
qPinch=0.98
qPinch=2.08
200 μs
Same simulation results
with very different
arc V/I characteristics
60 kA
40 kA
Existing P.S.
SC based P.S.
Ie
20 kA
0 kA
10 ms
1200 A
800 A
400 A
Lcoils = 14.2 mH
Rcoils = 70 mΩ
G. Maffia et al., EEEIC 2015, Rome
Phase-1
0 A
23

## Slide 24
Status
20 years after 2nd ST Workshop – Princeton (1995) the “aggressive proposal” PROTO-SPHERA
is producing its first centerpost plasmas …better late than never!
Hollow anode surprise, no anode arc attachment (electrostatic potential, E∧B plasma rotation)
(1/3) of the due current (10 kA) achieved, 3 kA sustained in Argon plasma
To achieve full current of 10 kA requires patient learning of how to tailor boundary conditions:
• electrostatic potential by connecting PF coils casings, built floating with respect to the vessel
• magnetic field by additional coils external to the vessel
• new Anode/Cathode “feed through” flanges in Polycarbonate, now in progress
After Argon centerpost is tamed (80 V breakdown), start fight with Hydrogen centerpost (180 V)
If full current of plasma centerpost (10 kA) is achieved and sustained with 54 sparsely spaced
emitting filaments, then full current (60 kA) will be even better achieved with 324 filaments
First stage of PROTO-SPHERA only an appetizer for the production of the Spherical Torus
…放龙入海!
…give a chance to the dragon to show his endowments into the sea!
24

## Slide 25
Perspective
Proto-Sphera will assess a new magnetic confinement configuration
• simply connected (easier construction & maintenance)
• with high plasma beta (minimal geometrical size)
• sustained by helicity injection
Proto-Sphera can develop this program:
at very modest costs (~ 1.6M€); in a flexible way (new components can be easily added)
Final PROTO-SPHERA will be much more demanding in manpower and effort
than the present phase-1 of PROTO-SPHERA with Centerpost plasma only
Will be an experiment even more challenging than START was for Culham
• with sophisticated control requests (very fast rise of currents for Torus formation)
• with demanding diagnostic requests
• challenging physicists, engineers and technologists creativity with its adaptability
25

## Slide 26
CKF configuration: a possible evolution of Proto-Sphera
CKF found to be ideally MHD stable up to β=1
…promising for future fusion space thrusters?
Degenerate X-point on Proto-Sphera anode is a nozzle?
?
Different orbits of co- & counter-circulating charged fusion products:
…preferential thrust through
one of the two degenerate X-points
How to drive the ST current?
In a D-He3 reactor the co- & counter-circulation of charged fusion products could produce the sustainment current of the surrounding plasma…
2015 experiment
Proto-Sphera: a CKF whose Surrounding Plasma terminates upon electrodes
and whose Secondary Tori are substituted by PF2/3 poloidal field coils
26

## Slide 27
A pair of new coils, same electrodes:
smaller but hotter?
Proto-Sphera load assembly could in principle accommodate a CKF, with some changes,
in order to investigate formation, stability and β level before the resistive decay
Same coils, new electrodes:
bigger but colder?
CKF configuration: a possible evolution of Proto-Sphera
(continue…)
27

## Slide 28
Having produced a plasma, albeit only the centerpost one, we finally got
our star at the 2015 Princeton International Spherical Torus Workshop!
28