## Slide 1
Obtainment of the Phase1 full performances in
PROTO-SPHERA and future perspectives of the experiment
P. Micozzi1, F. Alladio, G. Apruzzese, L. Boncagni, O. D'Arcangelo, E. Giovannozzi, A. Grosso, M. Iafrati,
A. Lampasi, G. Maffia, A. Mancuso, V. Piergotti, G. Rocchi, A. Sibio, B. Tilia, O. Tudisco, V. Zanza
Centro Ricerche ENEA, Frascati C.P. 65, Rome, Italy 1e-mail: paolo.micozzi@enea.it

## Slide 2
PROTO-SPHERA key differences:
Substitute the Spherical Tokamak central rod with a Screw Pinch plasma
(ITF → Ie)
Flux Core Spheromak (FCS)
Theory: Taylor & Turner, Nucl. Fusion 29, 219 (1989)
Experiment: TS-3; N. Amemiya, et al., JPSJ 63, 1552 (1993)
But Flux Core Spheromaks are:
• injected by plasma guns
• formed by ~10 kV
voltage on electrodes
• high pressure prefilled
• with ST safety factor q≤1
PROTO-SPHERA concept
• PROTO-SPHERA formed “slowly”
as a prolated low aspect ratio
Spherical Torus from the
pre-existing plasma centerpost,
mushroom-shaped in front of electrodes
• At low voltage (~100 V), inside big vessel
• Designed for a Tokamak-like field-line
rotational trasform (q0 ≥ 1, qedge~ 3)
(aspect ratio A = R/a ≥ 1.2, elong. k = b/a ~ 2.3)
PROTO-SPHERA
TS-3
Tokio University
2
Potentially two conventional ST problems solved:
• Simply connected configuration (no conductors inside)
• Ip driven by Ie (Helicity Injection from SP to ST)

## Slide 3
3
PROTO-SPHERA
Centerpost current Ie= 60 kA
ST toroidal current Ip= 120÷240 kA
ST diameter 2Rsph= 0.7 m
Axisymmetric simulation of ST formation
Resistive MHD
simulations of
ST formation
Non-axisymmetric simulation of ST formation
Formation time scale (τAlfvén•τResist)1/2 ~ 0.6 ms
from τAlfvén ~ 0.5 μs
τResist ~ 70 ms
Garcia-Farengo, PoP 16,112508 (2009)
and
Ricardo Farengo, ISTW2008 - Frascati

## Slide 4
4
Anode
Magnetic
reconnection
Cathode
• In front of the electrodes:
open magnetic field lines,
into closed , lines
wrapped around the spherical torus
• Magnetic reconnections convert
open lines
• Open magnetic field lines are wound
in a circular direction
of Tokamaks relies on induction of PROTO-SPHERA relies on
efficient but not forever… associated with magnetic reconnections
SUSTAIN THE CONFINING CURRENT:
by DC voltage from anode to cathode
HOW EFFICIENT THE SUSTAINMENT OF TOROIDAL CURRENT BY RECONNECTIONS?
Critical points of PROTO-SPHERA:
• IST= 240 kA (4xIe) really achievable?
• Can it be sustained by Helicity Injection
for at least τR~ 70 ms?
(machine designed for 1 sec sustainment!)
• Resistive MHD stability & confinement?
Magnetic
reconnection

## Slide 5
5
In 2002 at Frascati an International Workshop
advised to build the machine in 2 steps:
• Phase 1: demonstrate Plasma Centerpost’s feasibility
• Phase 2: machine completed such as to produce the Spherical Torus
Phase1: 8 PFcoils
Centerpost shape
Phase 2: 8 PF shaping coils
+ 10 PF compressing coils
SP centerpost current Ie= 8.5 kA
No ST toroidal current
SP centerpost current Ie= 60 kA
ST toroidal current Ip= 120÷240 kA
A→1.2
Ip=30 → 240kA
Ie=8.5 → 60kA
A=1.8
ST compression

## Slide 6
6
Cylindrical vacuum vessel was START vacuum vessel, donated by Culham in 2004
…from ideas …to detailed design …to hard metal
from Culham the old vacuum vessel found its road to Frascati
PROTO-SPHERA was built (2006-2009) by ASG Superconductors of Genoa, cost 1 M€
Years 2004 - 2010:
ASG 2007
ASG 2009

## Slide 7
7
Electrical power supplies built by EEI of Vicenza, cost 0.7 M€
Years 2011 - 2014:
Anode
PF2 coils
throttles
Cathode
To fire the plasma centerpost (Phase1)
3 Power supplies are required
• Cathode heating rotating 6-phase: 6 x(1.7 kA,25 V) rms
(18 modulus i.e. 1/6 with respect to Phase2)
• PF coils: 2kA, 350 V DC current
• Plasma centerpost: 10 kA, 350 V DC current
PROTO-SPHERA POWER SUPPLY
Cathode

## Slide 8
8
PF2up
PF2low
Status of art at EPR2016
Shot 208
October 2015 / January 2016
experiments with external PF coils:
Plasma current outer paths for I > 3.5 kA
Argon plasma
aiming to 4 kA
reaches 3.5 kA
~ 1.5 kA lost
from main plasma
in discharge from
cathode down to
lid\vessel
Shot 208
Also the Cathode emission lowers after 1.5 kA are lost
Shot 208
PF2up
PF2low
plasma fired after 0.75 s of PF current
(skin current time to remove X-point from inside vessel)

## Slide 9
9
PF2up
PF2low
On the top (near anode) a SS flange, pierced by 8 bus-bars, such a flange substituted by a 4 cm thick Polycarbonate one
Bus-bars (top-anode)
2015 experiments produced a heavy metallization on the top (anode) & bottom
(cathode) bus-bar vacuum entrance flanges, associated with magnetic “nozzles”
Top flange view from plasma side
Anode exit of nozzle
Geometry of magnetic nozzle
Anode

## Slide 10
10
PF2up
PF2low
June 2016: insertion of Polycarbonate (transparent) anode bus-bar flange on top of machine
4 cm thick Polycarbonate
(required by atmospheric pressure)
Heavily metallized
top & bottom bus-bar flanges

## Slide 11
11
PF2up
PF2low
At the bottom (near cathode) a SS flange, pierced by 14 bus-bars,
such a flange has been substituted by a Polycarbonate one
July 2016: Polycarbonate
flange on machine bottom

## Slide 12
12
PF2up
PF2low
Secondary discharges from electrodes hitting Al vacuum vessel wall (plenty of scars!)
Polycarbonate flanges got rid of all metallization from bus-bars:
2mm thick Polycarbonate lining covers the Al vacuum vessel
secondary
2mm thick
Polycarbonate
screen
surrounds
rear of anode
December
2016
Shot 378
October
2016

## Slide 13
13
PF2up
PF2low
Shot 591
Shot 591
Secondary discharges hitting vacuum vessel wall
have been cured by Polycarbonate lining, but
1) Spurious plasma currents still flow outside the centerpost (albeit inside the vacuum vessel)
January 2017
patterns of spurious
currents are
either diffused
or filamentary
Input 0.6 MW
7 kA from power supply
Centerpost drives 60%
Shot 597
crisis
Shot 591
PF2up
PF2low

## Slide 14
14
PF2up
PF2low
Shot 567
Secondary discharges hitting vacuum vessel wall
have been cured by Polycarbonate lining, but
2) in Hydrogen (250 V breakdown) there was still a problem of current through the vessel,
this was triggered in Argon (80 V breakdown), connecting the common star potential of the six-phased cathode power supply to the machine GND
Most critical electric field is
at contact between SS upper
extension & Al vacuum vessel
A spacing insulating ring
was inserted in May 2017
January 2017

## Slide 15
15
PF2up
PF2low
Shot 567
Shot 567
Shot 567
To avoid the flowing of plasma currents outside the desired path of the plasma centerpost two large insulating polycarbonate diaphragm separators have been inserted
to avoid the bus-bar to vessel current flow an insulating
spacer ring has been inserted
May 2017: Insertion of
Polycarbonate lower diaphragm
lower
diaphragm
lower
diaphragm
lower
diaphragm
Lower spacer ring not yet inserted

## Slide 16
16
PF2up
PF2low
Shot 567
Shot 567
Shot 567
upper diaphragm
lower diaphragm
PF2up
PF2low
upper
diaphragm
upper
diaphragm
spacer ring
spacer ring
May 2017: Insertion of
Polycarbonate upper diaphragm
& Polycarbonate spacer ring
1-2 mm clearance
1-2 mm clearance

## Slide 17
17
PF2up
PF2low
Shot 567
Shot 567
Shot 567
Some spurious and concentrated plasma current still sneaks through the narrow clearance (1-2 mm) between polycarbonate cylindrical lining and diaphragm,
plasma currents with 8.6 kA through PF2 are achieved
Power input 1.65 MW, Anode-cathode voltage 195 V
With currents through PF2 exceeding ~ 6kA the
rotational transform of plasma centerpost (q ~ 2.5-3)
becomes clearly visible…
The plasma centerpost seems to rotate azimuthally ( )
in clockwise direction (looking from above)
(…the six-phased cathodic rotation is switched off…)
June 2017 Plasma with Polycarbonate two diaphragms & upper Polycarbonate spacer ring
High currents (8 kA), external PF coils are on
Shot 614
PF2up
PF2low
the spurious plasma current closes on the
outside of PF2low, producing bright filaments

## Slide 18
18
PF2up
PF2low
Shot
Shot 567
Shot 567
PF coils casings built as floating
Electrostatic potential is dominated by the plasma; PF coils casings better left floating!
Upper lid & extension also better left floating! through Polycarbonate spacer ring
VPF4up ~ 130 V
Vanode ~ +150 V
VPF2-3up ~ +75 V
VPF2-3low ~ +20 V
Vcathode ~ -45 V
VPF4low ~ -7 V
vacuum vessel at GND (0 V)
#614 8.6kA Argon
Plasma centerpost
June 2017
upper lid & extension float at 90 V
Lines: magnetic field Color contours: electrostatic potential, Arrows: E field
High currents (8 kA), switching on the external PF coils:
PF2low
PF3.1low
PF4.2low
Cathode
PF4.1low
Ext.Coil low
Ext.Coil up
PF2up
PF3.1up
Anode
PF4.2up
PF4.1up
Strong toroidal rotation due to
prevents any anchoring on Anode!

## Slide 19
19
PF2up
PF2low
Shot
Shot 567
Shot 567
June 2017
Switching off the external PF coils it is possible to have a more uniform distribution of the spurious plasma current that sneaks through the narrow clearance (1-2 mm) between polycarbonate cylindrical lining and diaphragm, however in this
case the plasma currents through the PF2 coils reduces to ~ 6kA
It is quite evident that the plasma that sneaks through the upper narrow clearance corresponds to the bright filaments on the outside of PF2low, which diffuse towards the clearance
Shot 665
PF2up
PF2low

## Slide 20
20
PF2up
PF2low
Shot
Shot 567
Shot 567
vacuum vessel at GND (0 V)
upper lid & extension floating 78 V
PF2low
PF3.1low
PF4.2low
Cathode
PF4.1low
Ext.Coil low
(off)
Ext.Coil up
(off)
PF2up
PF3.1up
Anode
PF4.2up
PF4.1up
#665 6kA Argon
Plasma centerpost
June 2017
Strong toroidal rotation due to
prevents any anchoring on Anode!
VPF4up ~ +98 V
Vanode ~ +135 V
VPF2-3up ~ +65 V
VPF2-3low ~ +4 V
Vcathode ~ -45 V
VPF4low ~ -13 V
PF coils casings built as floating
Electrostatic potential is dominated by the plasma; PF coils casings better left floating!
Upper lid & extension also better left floating! through Polycarbonate spacer ring
Lower currents, switching off the external PF coils:
Lines: magnetic field Color contours: electrostatic potential, Arrows: E field

## Slide 21
21
Switching off the external PF coils, long duration plasma centerposts have been obtained with plasma currents through the PF2 coils ~ 6 \ 7 kA
This plasma centerpost discharge is quite near to
the rotational trasform value ι ~ ½  (qPinch ~ 2)
June 2017
Lower currents, switching off the external PF coils
0.7 s long discharge
Shot 644
PF2low
PF2up

## Slide 22
22
Reducing by a factor of 4 the magnetic field of the internal PF coils, the plasma centerpost has been destabilized
A long duration kink-bended plasma centerpost has been obtained with plasma currents through the PF2 coils ~ 5 \ 6 kA
This plasma kink-bended centerpost discharge survives
at a rotational trasform value ι ~ 1.66  (qPinch ~ 0.6)
The anode plasma wobbles gently
Cathode plasma wobbles more than centerpost, but
the discharge survives till the DC voltage is applied!
June 2017
Kink destabilization maintained in 0.7s long discharge
Shot 645
PF2low
PF2up

## Slide 23
23
Physics Design
1997-2008
Experiment
2017
PROTO-SPHERA
destabilization

## Slide 24
24
The plasma current sneaking through the narrow clearance (1-2 mm)
between polycarbonate cylindrical lining and diaphragm induces damages
The narrow clearance has
to be closed completely by
a bonding material
able to sustain the diaphragms weight
The port where the polycarbonate lining was cut, in order to allow for
vacuum gauges measurements,
has to be closed
& the gauges moved elsewhere

## Slide 25
25
#649 kA Argon Plasma centerpost (June 2017)
Disaster if top lid & top extension are not floating!
Color contours: electrostatic potential, Arrows: E field Lines: magnetic field
Polycarbonate spacer ring insulating top lid and top extension from vessel (GND)
have been put back in contact with vessel

## Slide 26
26
spacer ring
June 2017: Polycarbonate spacer ring insulates top lid and top extension from vessel (GND)
if they are put back in contact with vessel, plasma centerpost current through PF2 is hampered
 Large part of current flows into vacuum vessel  secondary discharges bus-bars  vessel
Top extension
Vessel (GND)
Plasma current reaches 6 kA,
but after secondary discharges current drops to 3 kA
To achieve full centerpost current in Hydrogen (250 V break-down) needs a new insulating vacuum vessel
Shot 649
PF2low
PF2up

## Slide 27
27
Shot 649
PF2low
PF2up
If whole current of power supply (10 kA) is successfully driven in the Argon centerpost plasma it will be necessary to substitute the Al vacuum vessel with
a Polymetacrylate (PPMA) transparent and insulating vessel (5 cm thick, 2m , 1.6 m high)
adding 2 further SS rings on top & bottom of the experiment,
keeping all internal components attached to the existing SS upper\lower lid and extension
then try Hydrogen plasma
flanged PPMA cylinder carved PPMA cylinder
A new insulating & transparent vacuum vessel has to be built: will be Phase-2 ready

## Slide 28
28
Shot 649
PF2low
PF2up
To be build, after 10 kA plasma centerpost routinely achieved,
full PROTO-SPHERA load assembly and power supplies
Group A: ST compression coils (5+5 series)
Not yet built, but inner vessel ready to host
• high voltage (~ 20 kV) insulation
thin Inconel casings cost ~ 0.5M€
Final Power Supplies for:
1) Group A PF coils cost ~ 0.1M€
2) Cathode (Icath 10 → 60 kA) cost ~ 0.2M€
3) Centerpost (Ie 10 → 60 kA) cost ~ 0.6M€
SuperCapacitors will be used
Tungsten filaments (54 → 324) cost ~ 0.2M€
Cost up to now ~ 2.0 M€
Cost for final stage of experiment ~ 1.6 M€

## Slide 29
29
Shot 649
PF2low
PF2up
Perspectives
Proto-Sphera will assess a new magnetic confinement configuration, potentially stationary
Power injected into the centerpost
should be > 250 V • 60 kA = 15 MW…
It is a huge power into such a small plasma
…however how much will go into
the confining Spherical Torus,
through magnetic reconnections?
No one is able to predict:
• should it be zero, then ST plasma T = 10 eV
PROTO-SPHERA studies plasma-electrode interactions
• should it be 1 MW, then ST plasma T ~ 100 eV
PROTO-SPHERA studies magnetic reconnections
at relevant magnetic Lundquist number, S~105
• should it be many MW, then ST plasma T ~ 1 keV
…β ~ 1 !
…would do as a Tokamak, but at 1/100 of the cost
Status (June/July 2017)
• Hollow anode surprise, no anode arc attachment (electrostatic potential,
E x B plasma rotation)
• 8.6 kA achieved (10 kA available from power supply), 7 kA sustained 0.7 s in Argon plasma
• Preliminary measurements with Langmuir probes (in the anode zone): Te≈8-10 eV, n > 1019 m-3
• After Argon centerpost is tamed
(80 V break-down, 2 MW), build new insulating & transparent vessel, then tame Hydrogen centerpost
(250 V break-down, 3MW?)
• If full current of plasma centerpost
(10 kA) is achieved and sustained with 54 sparsely spaced emitting filaments, then full current (60 kA) will be even better achieved with 324 filaments

## Slide 30
30
+ Other
authors